Final settling tank

Purpose:

1- Clarifying the waste water from all suspended matters organic and inorganic. 
2- Sediment the suspended matters to return a part of it to achieve the oxidization process.

Design criteria: ( in case of aeration tank)

Qd = Q + Qr.s   m³/d

Solid load = 3 kg/m²/hr at average flow

= 8 kg/m²/hr at peak flow

No. of final settling tank ( F.S.T ) ≥ 2

d = 2.5 – 4.5 m

Φ ≤ 40 m

Hydraulic weir loading = 100 – 150 m³/m/d

Surface loading rate = 16 - 32 m³/m²/d at average flow

= 40 – 50 m³/m²/d at peak flow

T = V / Qd        ( 2 - 3 hrs )

Design criteria: ( in case of trickling filter)

Qd = Q + QR   m³/d

T = 1.5 – 2 hr

d = 3 – 3.5 m

No. of final settling tank ( F.S.T ) ≥ 2

Φ ≤ 40 m

Hydraulic weir loading = 100 – 150 m³/m/d

Surface loading rate = 16 - 32 m³/m²/d at average flow

= 40 – 50 m³/m²/d at peak flow

Example:

A sewage treatment plant of daily discharge 18000 m3. Find the numbers and dimensions of final settling tanks if the secondary treatment is high rate trickling filters if:

- Row sewage BOD5 =250 mg/l

- Effluent BOD5 = 40 mg/l

- BOD5 removal efficiency of primary sedimentation= 30%

- Recirculation ratio (R) is 1.5 the design flow.

Solution:

Qd = Q + QR

= 18000 + 1.5 x 18000 = 45000 m3/d

V = Qd x T                         assume T = 2 hr

= 45000 x 2/24 = 3750 m3

Assume d = 3.5 m

Example:

Determine the volume and dimensions of final settling tank after aeration tanks. Which is designed to treat the flow Q = 12000 m3/d. Given the following data:

- MLVSS in aeration tank (X) = 2500 mg/l

- MLSS in return sludge = 8000 mg/l

Solution:

Qd = Q + Qr.s

Example:

For the last example design contact tanks.

Solution:

Qd = 12000 m3/d

T = 15 – 20 minutes

# Text boxes

Final settling tank

QR=RxQd

BOD2

Q + QR

BOD1

Q

H.R.T.F

F.S.T

P.S.T

Q

pump

Q

Effluent

Excess sludge

Qw

Xr

QR.S  ,   Xr

Q+QR.S

Q=12000

F.S.T

A.T

X=2500

P.S.T

1.5m

2m

Length

of paths

2m

Purpose:

Destroy bacteria.

Design criteria:

Chlorine dose = 2 – 10 P.P.M

T = 15 – 20 minutes

n ≥ 2

V per tank = 2 x 1.5 x length of paths x No. of paths

No. of paths = 8 – 10 channels

Contact tank

Chlorine gas

Contact tank