Sewerage System

Sewerage system components

1- Gravity collection system.

Gravity system consists of sewers and inspection chambers (manholes).

2- Waste water pump station.

Waste water pump station consists of pumps, valves, suction pipes, delivery pipes and discharge gauge.

3- Force main or rising main.

categories of sewers :

- building sewers

- lateral sewers

- main sewers

- interceptor

Types of sewerage systems:

1- Combined sewerage system:

Combined system requires only one sewer in a street which is an important consideration in streets which are crowded with under ground pipes for water, telephone, electric cables and other utilities.

2- Separate sewerage system:

It is used in rainy cities which the quantities of domestic wastewater in only a small fraction of the storm water.

A comparison between the combined system and the separate system

| Combined system | Separated system |
| --- | --- |
| Small quantity of rain | large quantity of rain |
| Narrow streets | Wide streets |
| The land is flat | The land had a great slops |
| Concentrated wastewater | A near place for disposal is available |

The design criteria of sewers:

1- Sewers should run partially full.

Sewers of diameter ≤ 375 mm run ½ full.

Sewers of diameter › 375 mm and ≤ 700 mm run 2/3 full.

Sewers of diameter › 700 mm run 3/4 full.

2- Maximum velocity in sewers should not exceed the velocity that damages the sewer which is 2 m/s.

3- Minimum velocity in sewers should not go below 0.45 m/s.

4- Minimum cover should not be less than 1.2 m.

5- Maximum excavation should not exceed 5 – 7m depend on the type of soil.

6- Minimum diameter of sewer is 7” and preferably 8”.

Types of sewers material:

| Sewer type | Diameter (mm) |
| --- | --- |
| Glass vitrified clay G.V.C | 175 – 900 |
| U.P.V.C | 200 – 700 |
| Polly ethylene high density | 200 – 700 |
| G.R.P | 200 – 2800 |
| Ductile cast iron | 200 – 900 |
| Pre-cast concrete | 600 – 3000 |

Sewer used in sewerage system

| Sewer usage | Sewer type |
| --- | --- |
| House connection | Glass vitrified clay G.V.C – U.P.V.C - Polly ethylene high density |
| Lateral sewer | Glass vitrified clay G.V.C – U.P.V.C - Polly ethylene high density – G.R.P – reinforced concrete |
| Main sewer |  |
| Collector – interceptor | G.R.P – reinforced concrete |
| Force main | Ductile cast iron - GRP –pre-stressed concrete |
| Pipes in pump station | Ductile cast iron - steel |
| Pipes in valves room | Ductile cast iron - steel |
| Pipes between wastewater treatment plant's units | Ductile cast iron - steel |

The design flow rates of the sewerage system:

Sewage factor = 0.8 – 0.9.

Qave = (0.8 – 0.9) qave x population.

Qave summer = (1.2 – 1.3) Qave

Qave winter    = (0.7 – 0.8) Qave

Qmax summer = P.F.F x Qave summer + Qinf

Qmax winter    = P.F.F x Qave winter + Qinf + QR

Qmin winter     = M.F.F x Qave winter + Qinf + QR

For population > 80000

For population ≤ 80000

m = coefficient depends on sewer types and age.

= 0.2 – 0.5 for cast iron.

= 1 – 10 for G.V.C

d = diameter in inches.

Y = depth of water above the center line of the sewer

Qinf = 15% of Qave

I = intensity of rain (mm/day)

R= run off factor

= ½  - 1/3 for roods.

= 1/6 – ¼ for roves.

A= area in hectares

Hydraulic design of sewerage system

The equations used in the design of sewers:

1- Q = Awet x v                                   discharge equation

2- v = 1/n R2/3  S1/2                                          Manning equation

v: velocity

n: coefficient of roughness (n=0.012 – 0.15)

R: hydraulic radius (R = Awet/pwet)

S: slope (s=h/l)

3- v = 0.849 x C x R0.64 x S0.54     Hazen William equation

Chart (1)

In this chat we must use Qfull or vfull.

We can’t use this chart to get Qmax, Qmin, vmax, and vmin.

We have to have two parameters to get the other two parameters.

Chart (2)

In this chart if we know one parameter we can get the other two parameters .

Example:

A circular sewer carries 50 l/s when the sewer is full, and the flow is running 2/3 full, S = 3%◦. Determine the minimum velocity and depth of flow.

Solution:

From chart (1):

Qfull = 50 l/s , S = 3%◦         ( ( =12’’, vfull = 0.68 m/s

From chart (2):

(d = 2/3 x 12” = 8”

= 8 x 2.54 = 20.32 cm

(V = 0.68 x 1.08 = 0.73 m/s

Inspection chambers (manholes)

| (” | Distance (m) |
| --- | --- |
| 8 | 30 |
| 10 | 40 |
| 12 – 16 | 50 |
| 18 – 36 | 60 |
| 36 – 48 | 100 |
| ›48 | 150 |

# Text boxes

Interceptor Sewer

Lateral Sewer

To next Manhole

House

House Connection

Manhole

Collector Sewer

Main Sewer

Location of manholes:

1- Change in slope                                                 2- Change in direction

3- Intersections of sewers                                         4- Change in diameter

`

5- In case of steep slope

6- at regular distance depends on sewer diameter