Wastewater Treatment

Primary treatment:

The treated wastewater must be disposed in the sea.

Primary + Secondary treatment:

The treated wastewater can be disposed to drain.

Primary + Secondary + tertiary treatment:

The  treated wastewater may be used for irrigation.

Primary wastewater treatment:

Purpose :

Removal of settleable suspended solids (organic or inorganic).

Flow line in wastewater treatment plant

Deceleration tank:

Purpose:

Reduce the velocity of the sewage before screen to prevent escaping of removal matters.

Design criteria:

1- T = 5 - 60 sec 
2- V = 0.6 - 1.2 m/s 
3- L = 3 B

4- Qd = Qmax summer

= 0.8 x P.F.F x 1.2 x Qave

Qmin = Qmim winter

= 0.8 x M.F.F x 0.7 x Qave

Screen:

Purpose:

Removal of large floating objects such as plastic, metals, wood, paper….ext.

Types of screen:

With regard to spacing between bars:

1- Coarse screen: spacing between bars 2.5 – 7.5 cm (5 cm).

2- Fine screen:  spacing between bars 1 - 5 cm (2.5).

With regard to cleaning: 
1- Manual screen 
2- Mechanical screen.
 Design criteria:

1- Net area = (2 - 3) area of approach channel

2- Ө = 30◦ - 60◦

3- Depth of screen = depth of approach channel

4- No. of screens ≥ 2

5- Dimension of bars 
Ф (diameter of bars) = 10 - 19 mm 
S (spacing between bars) = 2.5 - 5   cm

6- Horizontal velocity before screen V1 ≥ 0.6 m/s

7- Velocity through screen V2 ≤ 1.5 m/s

Example:

For a city of average water consumption 250 l/c/d and population 400000 capita. Design the primary treatment units.

Solution:

Design of approach channel:

Assume v= 1.2 m/s

Qd = A x v

A = Qd / v

= 1.75 /1.2 = 1.46 m2

A = b x d

For best hydraulic section b =2d

A = 2d x d

1.46 = 2d2

d = 0.85 m                , b = 2 x 0.85=1.7 m

Area actual = b x d = 0.85 x 1.7 = 1.45 m2

Design of deceleration tank:

Assume T=30 sec                          T= 5 – 60 sec

V= Qd x T

= 1.75 x 30 = 52.5 m3

Assume L = 3 B

d = depth of approach channel = 0.85 m

V = A x d

52.5 = 0.85 x B x 3B

B = 4.53 m        , L = 13.61 m

Design of screen:

Assume:

- Net submerged area of screen = 2 x area of approach channel

- Depth of wastewater in screen (d) = depth of wastewater in approach channel.

=  0.85 m

- Spacing between bars = 5 cm

- Width of bars = 10 mm = 1 cm

- Length of submerged screen (L) = d / sin(

= 0.85 / sin 45◦ = 1.2 m

Area of spacing = L x b

= 1.2 x 0.05 = 0.06 m2

Net submerged area = 2 x A of approach channel

= 2 x 1.45 = 2.9 m2

No. of spacing = net submerged area / area of one spacing

= 2.9 / 0.06 = 48 space

Take 2 screens

No. of spacing in each screen = 24 space

No. of bars = No. of spacing + 1

= 24 + 1 = 25 bars

Width of screen (B) = total width of spacing + total width of bars

= 24 x 0.05 + 25 x 0.01 = 1.45 m

Chicks:

# Text boxes

Wastewater treatment

works

Disposal

or reuse

Collection

works

Primary

treatment

Territory

treatment

Biological

treatment

wwp

Primary sedimentation                              tank

Grit removal

chamber

Screen

Deceleration

tank

Approach channel

Force main

Mechanical screen

d

b

Approach channel:

Purpose:

Transmit sewage to screen with suitable velocity.

Design criteria:

1- velocity = 0.6 - 1.5  m/sec

V = 1/n R2/3 S ½                n = 0.015

2- Qd = Qmax summer

= 0.8 x P.F.F x 1.2 x Qave

Qd = A.V

A = b x d                b = 2d                     (  A = 2 d²

To get Smin assume Vmin = 0.6 m/sec

P.S

Manual screen