Wastewater

Sources of wastewater:

1- Domestic wastewater.

2- Industrial wastewater.

3- Storm water.

4- Infiltration water.

5- Commercial and governmental

Schematic diagram of a typical combined sewerage system

Composition and characteristics of wastewater:

Physical characteristics:

1- Total solids.

Sewage is 99.9% water and 0.1% solids.

2- Color: Gray tends to black.

3- Temperature: from 15 to 25 ◦C.

4- Odor: offensive.

Odor of domestic wastewater caused by gases produced due to the decomposition of organic matter. The most odorous gas in septic wastewater hydrogen sulfide (H2S).

5- Density: 1.02 – 1.05 t/m3.

6- Turbidity.

Chemical characteristics:

1- pH : 6 – 8.

2- Biological oxygen demand (BOD):

It is the amount of oxygen required by the bacteria to stabilize the organic matter in wastewater, under standard conditions of incubation at 20 ◦C for five days.

3- Chemical oxygen demand (COD):

It is the amount of oxygen required to stabilize all organic matter (bio-degradable and non biodegradable) chemically by strong chemical oxidizing agent.

COD : BOD

3    :    2

4- Ammonia- nitrogen

5- Nitrites and nitrates

6- Chlorides

7- Hydrogen sulfide

Biological characteristics:

Wastewater contains bacteria, fungi, algae, protozoa, viruses and pathogen bacteria.

Pathogen indicator:

E-coli, coli form, and fecal coli form.

# Text boxes

Inorganic 5 %

Organic 10 %

Inorganic 5 %

Organic 10 %

Inorganic 40%

Organic 30%

Non settleable

Settleable

Dissolved 70%

Suspended 30 %

Total solids

Protozoa

Fungi

Algae

Multicellular

Unicellular

Coli-form

Worm

Plants

Protests

Animal

Microorganisms

Bacteria