## Slide 1: Computer Organization
2015 - 2016

## Slide 2
Input/Output

## Slide 3: Basic Input/Output Operations
Input/Output operations which transfer data from the processor or memory to and from the real world are essential.
In general, the rate of transfer from any input device to the processor, or from the processor to any output device is likely to the slower than the speed of a processor.
  The difference in speed makes it necessary to create mechanisms to synchronize the data transfer between them.

## Slide 4: Basic Input/Output Operations (cont.)
Let us consider a simple task of reading a character from a keyboard and displaying that character on a display screen.
A simple way of performing the task is called program-controlled I/O.
There are two separate blocks of instructions in the I/O program that perform this task:
  One block of instructions transfers the character into the processor.
  Another block of instructions causes the character to be displayed.

## Slide 5: Basic Input/Output operations (cont.)
D
A
T
AIN
D
A
T
A
OUT
SIN
SOUT
K
e
yboard
Display
Bus
Processor
Input:
When a key is struck on the keyboard, an 8-bit character code is stored in the buffer register DATAIN.
A status control flag SIN is set to 1 to indicate that a valid character is in DATAIN.
A program monitors SIN, and when SIN is set to 1, it reads the contents of DATAIN.
When the character is transferred to the processor, SIN is automatically cleared.
Initial state of SIN is 0.

## Slide 6: Basic Input/Output operations (cont.)
D
A
T
AIN
D
A
T
A
OUT
SIN
SOUT
K
e
yboard
Display
Bus
Processor
Output:
When SOUT is equal to 1, the display is ready to receive a character.
A program monitors SOUT, and when SOUT is set to 1, the processor transfers a
character code to the buffer DATAOUT.
Transfer of a character code to DATAOUT clears SOUT to 0.
Initial state of SOUT is 1.

## Slide 7: Basic Input/Output operations (cont.)
Buffer registers DATAIN and DATAOUT, and status flags SIN and SOUT are part of a circuitry known as device interface.
To perform I/O transfers, we need machine instructions to:
  Monitor the status of the status registers (SIN and SOUT).
  Transfer data among the I/O devices and the processor.
Instructions have similar format to the instructions used for moving data between the processor and the memory.

## Slide 8: Accessing I/O devices
Bus
I/O de
vice 1
I/O de
vice
n
Processor
Memory
Multiple I/O devices may be connected to the processor and the memory via a bus.
Bus consists of three sets of lines to carry address, data and control signals.
Each I/O device is assigned an unique address.
To access an I/O device, the processor places the address on the address lines.
The device recognizes the address, and responds to the control signals.

## Slide 9: Accessing I/O devices (cont.)
I/O device is connected to the bus using an I/O interface circuit which has: Address decoder, control circuit, and data and status registers.
Address decoder decodes the address placed on the address lines thus enabling the device to recognize its address (each device has a unique address).
Data register (DATAIN and DATAOUT) holds the data being transferred to or from the processor.
Status register (SIN and SOUT) holds information necessary for the operation of the I/O device.
Data and status registers are connected to the data lines.
control circuit receive and transmit the control signals through the control line.

## Slide 10: Accessing I/O devices (cont.)
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input devices
Bus
Address lines
Data lines
Control lines

## Slide 11: Accessing I/O devices (cont.)
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Output devices
Bus
Address lines
Data lines
Control lines