## Slide 1: Computer Organization
2015 - 2016

## Slide 2: Instruction Set Architecture (ISA)
Instruction Set Architecture (ISA), or simply Architecture, of a computer is the interface between the hardware and the lowest-level software
ISA encompasses all the information necessary for programmers to write a machine language program that will run correctly, including instructions, registers, memory access, I/O devices, etc.
ISA allows computer designers to talk about functions independently from the hardware that performs them

## Slide 3: Instruction Set Architecture (ISA) (cont.)
Application Binary Interface (ABI) is the combination of the basic instruction set and the OS interface provided for application programmers
ABI is the user portion of the instruction set plus the OS interfaces used by application programmers
Binary compatibility is extraordinarily important! It enables upgrading the computer without having to replace software

## Slide 4: Interrupts
Normal execution of programs may be interrupted if some device requires urgent servicing
  To deal with the situation immediately, the normal execution of the current program must be interrupted

## Slide 5: Interrupts (cont.)
Procedure of interrupt operation
  The device raises an interrupt signal
  The state of the processor is first saved before servicing the interrupt
    Normally, the contents of the PC, the general registers, and some control information are stored in memory
  The processor provides the requested service by executing an appropriate interrupt-service routine
  When the interrupt-service routine is completed, the state of the processor is restored so that the interrupted program may continue

## Slide 6: Classes of Interrupts
Program
  Generated by some condition that occurs as a result of an instruction execution such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, or reference outside a user’s allowed memory space
Timer
  Generated by a timer within the processor. This allows the operating system to perform certain functions on a regular basis

## Slide 7: Classes of Interrupts (cont.)
I/O
  Generated by an I/O controller, to signal normal completion of an operation or to signal a variety of error conditions
Hardware failure
Generated by a failure such as power failure or memory parity error

## Slide 8: Performance

## Slide 9: Introduction
Performance is the key of the effectiveness of an entire system of hardware and software
choosing among different computers based on their performance
To improve the performance of a software system, we need to know:
– what hardware factors contribute to overall system performance
– the relative importance of these factors

## Slide 10: Measuring Performance
Program execution time is the measure of computer performance:
– Also known as response time, elapsed time, or latency
– It is the time between the start and completion of a task
– Measured in seconds per program
– The computer that performs the same amount of work in the least time
is the fastest
– Important for individual computer users

## Slide 11: Measuring Performance (cont.)
Throughput or bandwidth could also be used to measure performance:
– It is the total amount of work done in a given time
– Important for datacenter managers
Decreasing execution time almost always improves throughput
Changing either execution time or throughput often affects the other

## Slide 12: Measuring Performance (cont.)
CPU execution time (simply CPU time)
• the actual time the CPU spends computing a task’s lines of code
• does not include time spent waiting for I/O activities or running other programs

## Slide 13: CPU Time
CPU time can be further divided into:
– User CPU time
• the CPU time spent in the program itself
• expresses CPU performance
– System CPU time
• the CPU time spent in the OS performing tasks on behalf of
the program

## Slide 14: Exercise (1)
Do the following changes to a computer system decrease response time, increase throughput, or both?
Replacing the processor in a computer with a faster version
Both response time and throughput are improved

## Slide 15: Exercise (1) (cont.)
Adding additional processors to a system that uses multiple processors for separate tasks, e.g., searching the WWW
• No one task gets work done faster
• Only throughput increases
• If demand for processing is as large as the throughput, the system might force requests to queue up
• In this case, increasing the throughput could also improve response time, since it would reduce the waiting time in the queue

## Slide 16: Defining Performance
To maximize performance, minimize response time or execution time for some task
"X is n times faster than Y” means:

## Slide 17: Exercise (2)
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds
– How much faster is A than B?

## Slide 18: Exercise (3)
Computer C’s performance is 4 times faster than the performance of computer B, which runs a given application in 28 seconds
– How long will computer C take to run that application?

## Slide 19: Exercise (3)

## Slide 20: Clock Cycle
Clock cycles indicate when events take place in the hardware
Instead of reporting execution time in seconds, we often use cycles
We can count the number of CPU clock cycles for a program
Clock rate (clock cycles per second in MHz or GHz) is inverse of clock cycle time (clock period)

## Slide 21: Clock Cycle vs. Clock Rate
10 nsec clock cycle => 100 MHz clock rate
5 nsec clock cycle => 200 MHz clock rate
2 nsec clock cycle => 500 MHz clock rate
1 nsec (10-9) clock cycle => 1 GHz (109) clock rate
500 psec clock cycle => 2 GHz clock rate
250 psec clock cycle => 4 GHz clock rate
200 psec clock cycle => 5 GHz clock rate

## Slide 22: Clock Cycles Per Instruction
Different instructions take different amounts of time depending on what they do:
– Multiplication takes more time than addition
– Floating point operations take longer than integer ones
– Accessing memory takes more time than accessing registers
Instructions can be divided into classes of similar instructions
Instructions in the same class have the same Clock cycles Per Instruction (CPI) value

## Slide 23: CPU Clock Cycle
Total CPU clock cycles for a certain program can be calculated by looking at various instruction classes and their individual CPIs
– CPIi is the clock cycles per instruction for class i (integer number),
– Ci is the count of instructions executed from class i, and
– n is the number of instruction classes

## Slide 24: CPU Time
The CPU time for a program can be expressed in two ways:

## Slide 25: Exercise(4)
A program runs on computer A with a 2 GHz clock in 10 seconds. What clock rate must a computer B run at to run this program in 6 seconds? Unfortunately, to accomplish this, computer B will require 1.2 times as many clock cycles as computer A to run the program.

## Slide 26: Exercise(4)