## Slide 1: Computer Organization
2015 - 2016

## Slide 2: Instructions
Language of The Computer
(MIPS)

## Slide 3: Memory organization
  Information is stored in the memory as a collection of bits.
  Collection of bits are stored or retrieved simultaneously is called a word
  Number of bits in a word is called word length
  Word length can be 16 to 64 bits
  Collection of 8 bits known as a “byte”
  Word length of 16 bits, is equivalent to word length of 2 bytes
  Words may be 2 bytes (older architectures), 4 bytes (current architectures), or 8+ bytes (modern architectures).

## Slide 4: Memory organization (cont.)
Accessing the memory to obtain information requires specifying the “address” of the memory location
Addresses are assigned to a single byte. “Byte addressable memory”
Suppose k bits are used to hold the address of a memory location: size of the memory in bytes is given by 2k
For example, a 24-bit address generates an address space of 224 (16,777,216) locations (bytes)

## Slide 5: Memory Words

## Slide 6: Memory organization
Consider a memory organization:
16-bit memory addresses
Size of the memory is ?
216 Bytes
Word length is 4 bytes
Number of words = Memory size(bytes) = ?
Word length(bytes)
Word #0 starts at Byte #0.
Word #1 starts at Byte #4.
Byte 0
Byte 1
Byte 2
Byte 3
Byte 65535
Byte 65534
Byte 65533
Byte 65532
Word #0
Word #1
Word #?
Byte 4

## Slide 7: Execution of an instruction
The steps involved in the execution of an instruction by a processor:
  Fetch an instruction from the memory.
  Fetch the operands.
  Execute the instruction.
  Store the results.
Basic processor architecture has several registers to assist in the execution of the instructions.

## Slide 8: Registers in the control path
Instruction Register (IR):
  Instruction that is currently being executed.
Program Counter (PC):
  Address of the next instruction to be fetched and executed.
Memory Address Register (MAR):
  Address of the memory location to be accessed.
Memory Data Register (MDR):
  Data to be read into or read out of the current memory location, whose address is in the Memory Address Register (MAR).

## Slide 9: Basic Processor Architecture
Processor
Memory
PC
IR
MDR
Control
ALU
R(n-1)
-
R1
R0
MAR
n
general purpose
registers
Address of the memory
location to be accessed
Address of the next
instruction to be fetched
and executed.
Instruction that is
currently being
executed
Data to be read into or
read out of the current
location
General purpose
registers

## Slide 10: Basic processor architecture (cont.)
Control
Path
Data
Path
MAR
MDR
Memory
Processor
Control path is responsible for:
Instruction fetch and execution sequencing
Operand fetch
Saving results
Data path:
Contains general purpose registers
Contains ALU
Executes instructions

## Slide 11: Fetch/Execute cycle
Execution of an instruction takes place in two phases:
  Instruction fetch.
  Instruction execute.
Instruction fetch:
  Fetch the instruction from the memory location whose address is in the Program Counter (PC).
  Place the instruction in the Instruction Register (IR).

## Slide 12: Fetch/Execute cycle (cont.)
Instruction execute:
  Instruction in the IR is examined (decoded) to determine which operation is to be performed.
  Fetch the operands from the memory or registers.
  Execute the operation.
  Store the results in the destination location.
Basic fetch/execute cycle repeats indefinitely.

## Slide 13
Byte 0
Byte 1
Byte 2
Byte 3
Byte 65535
Byte 65534
Byte 65533
Byte 65532
Word #0
Word #1
Word #16383
Byte 4
MAR
MDR
Addr 65532
MAR register
contains the
address of the
memory location
addressed
MDR contains either the
data to be written to that
address or read from that
address.

## Slide 14
Notes: 1 --load
5-- add
2---store

## Slide 16: Addressing Modes
A high-level language enables the programmer to use constants, local and global variables, pointers, and arrays
When translating a high-level language program into assembly language, the compiler must be able to implement these constructs using the facilities in the instruction set of the computer
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes

## Slide 17: Addressing Modes (cont.)
Some of important addressing modes are:
  Immediate mode
  Register mode
  Absolute mode
  Indirect mode
  Index mode

## Slide 18: Addressing Modes (cont.)
Immediate mode
  Operand is given explicitly in the instruction.
  E.g. Move R0, 200
  Can be used to represent constants.
Register mode
  Operand is the contents of a processor register.
  Address of the register (its Name) is given in the instruction.
  E.g. Clear R1 or Move R1, R2

## Slide 19: Addressing modes (cont.)
Absolute mode
  Operand is in a memory location.
  Address of the memory location is given explicitly in the instruction.
  E.g. Clear A or Move R2, LOC
  Also called as “Direct mode” in some assembly languages

## Slide 20: Addressing Modes: Indirection and Pointers
Indirect mode:
  the effective address of the operand is the contents of a register or memory location whose address appears in the instruction
  Indirection is denoted by placing the name of the register or the memory address given in the instruction in parentheses
  The register or memory location that contains the address of an operand is called a pointer
  E.g. Move R1, (R2): in this case R2 contains the address of the operand to be loaded in R1

## Slide 21: Register Indirect Addressing Diagram

## Slide 22: Addressing Modes: Indexing and Arrays
Index mode
  the effective address of the operand is generated by adding a constant value to the contents of a register
  The index mode is useful in dealing with lists and arrays
  We denote the Index mode symbolically as X(Ri), where X denotes the constant value (offset) contained in the instruction and Ri is the name of the register involved.
  The effective address of the operand is given by EA=X+(Ri).
  E.g. Move R1, X(R2): in this case X+R2 represents the address of the operand to be loaded in R1

## Slide 23: Instruction types
Computer instructions must be capable of performing 4 types of operations.
Arithmetic and logic operations:
  E.g., addition, subtraction, comparison between two numbers.
Data transfer/movement between memory and processor registers.
  E.g., memory read, memory write
Program sequencing and flow of control:
  Branch instructions (decisions and loops)
Input/output transfers: to transfer data to and from the real world.

## Slide 24: MIPS Arithmetic operations
MIPS assembly language notation for arithmetic operations:
operation destination, source1, sourse2
Each MIPS arithmetic instruction performs only one operation
Each MIPS arithmetic instruction must have exactly three operands
Operand order is fixed (destination first)
The words to the right of the sharp symbol (#) are comments
Comments always terminate at the end of a line

## Slide 25: Exercise (1)
Write a MIPS assembly code that places the sum of the four integer variables b, c, d, and e into integer variable a, then subtracts integer variable f from a and puts the result in integer variable g
C code:
    a = b + c + d + e;
    g = a - f;

## Slide 26: Exercise (1) Sol.
C code:
  a = b + c + d + e;
  g = a - f;
MIPS code:
  add a, b, c # b + c → a
  add a, a, d # a + d → a
  add a, a, e # a + e → a
  sub g, a, f # a - f → g

## Slide 27: MIPS Operands
In MIPS, arithmetic instructions’ operands must be registers
MIPS has only 32 registers (limited number!) • For MIPS, a word is 32 bits (or 4 bytes) •
MIPS registers hold 32 bits of data (a word size)
MIPS is a general-purpose register architecture
  MIPS registers are general-purpose registers (GPRs)
  MIPS registers can be used for addresses or data with any instruction
It is the compiler’s job to associate program variables with registers

## Slide 28: MIPS Registers

## Slide 29: Exercise (2)
The following C statements contain the six integer variables e, f, g, h, i, j:
  f = (g + h) - (i + j);
  e = f;
Suppose that the compiler associates variables e, f, g, h, i, and j with registers $s0 through $s5, respectively
What is the compiled MIPS assembly code?

## Slide 30: Exercise (1) Sol.
C code:
  f = (g + h) - (i + j);
  e = f;
MIPS code:
  add $t0, $s2, $s3 # $t0 is a temporary register
  add $t1, $s4, $s5 # $t1 is a temporary register
  sub $s1, $t0, $t1
  add $s0, $s1, $zero # copy f ($s1) to e ($s0)

## Slide 31: Data Transfer Instructions
Data transfer instructions: transfer data between memory and registers
  load word (lw): copies a word from memory to a register
  store word (sw): copies a word from a register to memory
  lw $s0, c ($s1) # Memory [$s1 + c] → $s0
  sw $s0, c ($s1) # $s0 → Memory [$s1 + c]
    $s1 is the Index (base) register
    constant c is the offset
MIPS memory is only accessed through loads and stores

## Slide 32: Exercise (3)
Registers $s1 and $s2 of a computer contain the decimal values 1200 and 4600. What is the effective address of the memory operand in each of the following instructions? And explain their action.
  lw $S4,20($S1)
  sw $S5, 1000($S2)

## Slide 33: Exercise (3) Sol.
For the instruction: lw $S4,20($S1)
The address is:20+1200=1220
it reads the word in the memory location 1220 and loads it in the register $s4
For the instruction: sw $S5, 1000($S2)
The address is:1000+4600=5600
it writes the word in the register $s5 to the memory location 5600 and loads it in

## Slide 34: Exercise (4)
Lets also assume that the base address of the integer array d is in register $s4 and a value is in register $s1
Compile the following C statement into MIPS assembly code:
d[3] = d[2] + a;

## Slide 35: Exercise (4) Sol.
C code:
d[3] = d[2] + a;
MIPS code:
  lw $t0, 8($s4) # Memory [$s4 + 2*4] → $t0
add $t0, $t0, $s1 # $t0= $t0+ $t1
sw $t0, 12($s4) # $t0 → Memory [$s4 + 3*4]

## Slide 36: Exercise (5)
Lets assume that the compiler has associated integer variables h and i with registers $s2 and $s4, respectively
Lets also assume that the base address of the integer array A is in register $s3
Compile the following C statement into MIPS assembly code:
A[i] = h + A[8];

## Slide 37: Exercise (5) Sol.
C code: A[i] = h + A[8];
MIPS code:
  lw $t0, 32 ($s3) # Memory [$s3 + 8*4] → $t0
  add $t0, $s2, $t0 # h + A[8] → $t0
  add $t1, $s4, $s4 # $t1 = 2*i
  add $t1, $t1, $t1 # $t1 = 4*i
  add $t1, $t1, $s3 # $t1 = $s3 + 4*i (address of A[i])
  sw $t0, 0 (t1) # $t0 → Memory [$t1]