## Slide 1: Computer Organization
2015 - 2016

## Slide 2
The Processor 1

## Slide 3: Introduction
The implementation of the processor determines both the clock cycle time and the number of clock cycles per instruction (CPI)
We will be examining an implementation that includes a subset of the core MIPS instruction set:
  The memory-reference instructions: lw, sw
  The arithmetic-logical instructions: add, sub, and, or, slt
  The control flow (branch and jump) instructions: beq, j

## Slide 4: Introduction (cont.)
A simple implementation that uses a single long clock cycle for every instruction will be shown
  Every instruction begins execution on one clock edge and completes execution on the next clock edge
clock

## Slide 5: MIPS Summary

## Slide 6: MIPS Summary (cont.)
Instruction | Format | op | funct | Instruction | Format | op | funct
add | R | 010 | 3210 | lw | I | 35 | 
addi | I | 8 |  | nor | R | 0 | 39
and | R | 0 | 36 | or | R | 0 | 37
andi | I | 12 |  | ori | I | 13 | 
beq | I | 4 |  | sb | I | 40 | 
bne | I | 5 |  | sh | I | 41 | 
j | J | 2 |  | sll | R | 0 | 0
jal | J | 3 |  | slt | R | 0 | 42
jr | R | 0 | 8 | slti | I | 10 | 
lb | I | 32 |  | srl | R | 0 | 2
lh | I | 33 |  | sub | R | 0 | 34
lui | I | 15 |  | sw | I | 43 | 

## Slide 7: MIPS Summary (cont.)
MIPS Registers
Name | Register number (decimal) | Usage | Preserve on call?
$zero | 0 | the constant value 0 | n.a.
$at | 1 | reserved for the assembler | n.a.
$v0-$v1 | 2-3 | procedure return values and expression evaluation | no
$a0-$a3 | 4-7 | procedure arguments (parameters) | no
$t0-$t7 | 8-15 | temporary registers | no
$s0-$s7 | 16-23 | general purpose saved registers | yes
$t8-$t9 | 24-25 | more temporary registers | no
$k0-$k1 | 26-27 | reserved for the OS | n.a.
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | procedure return address | yes

## Slide 8: MIPS Summary (cont.)
Simplicity and regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes

## Slide 9: MIPS Summary (cont.)
  Immediate addressing: the operand is a constant within the instruction
addi $s1, $s2, 100
  Register addressing: the operand is a register
add $s1, $s2, $s3
  Base or Index addressing: the operand is at the memory location whose address is the sum of a register and a constant in the instruction
lw $s1, 100($s2)

## Slide 10: MIPS Summary (cont.)
  PC-relative addressing: the address is the sum of the current PC and a constant (multiplied by 4) in the instruction
beq $s1, $s2, 100
  Pseudodirect addressing: the jump address is a constant (26 bits) in the instruction (multiplied by 4) concatenated with the upper 4 bits of the PC
j 2500

## Slide 11: Clocking Methodology
There are two different types of logic elements:
  elements that operate on data values (combinational), e.g., ALU
  elements that contain state (sequential), e.g., memory and registers
A clocking methodology is used in synchronous systems to define when signals can be read and when they can be written
  Edge-triggered – all state changes occur on a clock edge
cycle time
rising edge
falling edge

## Slide 12: Clocking Methodology (cont.)
Typical execution
  read contents of state elements -> send values through combinational logic -> write results to one or more state elements
The time necessary for the signals to reach state element 2 defines the length of the clock cycle
The value stored in a state element is changed only when the write control signal is sent from the control unit and a clock edge occurs

## Slide 13: Clocking Methodology (cont.)
An edge-triggered methodology allows doing all of the following in the same clock cycle:
  reading the contents of a register
  sending the value read through some combinational logic
  writing back to that register

## Slide 14: Generic Implementation
  Fetch / Execute Cycle:
    use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
    decode the instruction (and read registers)
    execute the instruction
Fetch
PC = PC+4
Decode
Exec

## Slide 15: Generic Implementation (cont.)
There are some similarities across different instruction classes, e.g.,
  All instruction classes, except j, use the ALU after reading the registers:
    Memory-reference instructions use the ALU for an address calculation
    Arithmetic-logical instructions use it for the operation execution
    The branch instruction (beq) uses it for comparison

## Slide 16: Generic Implementation (cont.)
  After using the ALU, the actions required to complete various instruction classes differ:
    A memory-reference instruction accesses the data memory either to write data for a store or read data for a load
    An arithmetic-logical instruction writes the data from the ALU back into a register
    A branch instruction may need to change the next instruction address based on the comparison; otherwise the PC should be incremented by 4 to get the address of the next instruction

## Slide 17: Basic processor architecture
Control
Path
Data
Path
MAR
MDR
Memory
Processor
Control path is responsible for:
Instruction fetch and execution sequencing
Operand fetch
Saving results
Data path:
Contains general purpose registers
Contains ALU
Executes instructions

## Slide 18: Datapath Elements (1)
Datapath element: A functional unit used to operate on or hold data within a processor
Instruction memory:
  Stores and supplies the instructions of a program given an address
  No read signal is needed as it is read every clock cycle
  This memory is not written

## Slide 19: Datapath Elements (1) (cont.)
Program counter (PC):
  Holds the address of the current instruction (to be fetched)
  No write signal is needed as it is written every clock cycle
PC adder:
  Used to increment the PC to the address of the next instruction

## Slide 20: Fetching Instructions
Fetching instructions involves:
  reading the instruction from the Instruction Memory
  updating the PC value to be the address of the next (sequential) instruction
  PC is updated every clock cycle, so it does not need an explicit write control signal just a clock signal
  Reading from the Instruction Memory doesn’t need an explicit read control signal
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Fetch
PC = PC+4
Decode
Exec

## Slide 21: Fetching Instructions (cont.)
Thick lines (with no width indication) indicate buses of 32 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4

## Slide 22: Datapath Elements (2)
Register file:
  A collection of the processor 32 general-purpose registers in which any register can be read or written by specifying its number in the file
  The register file contains the register state of the computer
  Writes are controlled by the write control signal (RegWrite)

## Slide 23: Datapath Elements (2) (cont.)
Arithmetic and logic unit:
  The ALU is used to operate on the values read from the registers
  It takes two 32-bit inputs and produces a 32-bit result, as well as sets a 1-bit signal if the result is zero
  It is controlled by a 4-bit control signal (ALU operation)

## Slide 24: Decoding Instructions
Decoding instructions involves:
  sending the fetched instruction’s opcode and function field bits to the control unit then the control unit sends a 4 bit signal to ALU to determine the operation
  reading two values from the Register File
    Register File addresses are contained in the instruction
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit

## Slide 25: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform operation (op and funct) on values in rs and rt
  store the result back into the Register File (into location rd)
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10

## Slide 26: Executing R Format Operations (cont.)
I
n
s
t
r
u
c
t
i
o
n
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
W
r
i
t
e
d
a
t
a
A
L
U
r
e
s
u
l
t
A
L
U
Z
e
r
o
R
e
g
W
r
i
t
e
A
L
U
o
p
e
r
a
t
i
o
n
4

## Slide 27: Executing Load and Store Operations
Load and store operations involves:
  ALU compute memory address by adding the base register (read from the Register File during decode) to the 16-bit signed-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory (needs a read control signal(MemRead))
  load value, read from the Data Memory, written to the Register File (needs a write control signal(MemWrite))

## Slide 28: Executing Load and Store Operations (cont.)
I
n
s
t
r
u
c
t
i
o
n
1
6
3
2
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
D
a
t
a
m
e
m
o
r
y
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
W
r
i
t
e
d
a
t
a
S
i
g
n
e
x
t
e
n
d
A
L
U
r
e
s
u
l
t
Z
e
r
o
A
L
U
A
d
d
r
e
s
s
M
e
m
R
e
a
d
M
e
m
W
r
i
t
e
R
e
g
W
r
i
t
e
A
L
U
o
p
e
r
a
t
i
o
n
4

## Slide 29: Executing R-type instructions and memory instructions:

## Slide 30: add $s0, $s1, $s2
$s1
$s2
$s0
$s1 content
$s1 content + $s2 content
Write the result to register $s0
$s2 content

## Slide 31: addi $s0, $s1, 20
$s1
$s0
$s1 content
$s1 content + 20
Write the result to register $s0
32 bit represents 20
16 bit represents 20

## Slide 32: lw $s0, 100($s1)
$s1
$s0
$s1 content
16 bit represents 100
32 bit represents 100
Calculated memory address
memory address content
Write memory address content to register $s0

## Slide 33: sw $s0, 100($s1)
$s1
$s0
$s1 content
16 bit represents 100
32 bit represents 100
Calculated memory address
Data to be written in the memory address