## Slide 1: Logic Gates
Dr.Ahmed Bayoumi
Dr.Shady Elmashad

## Slide 2: Objectives
Identify the basic gates and describe the behavior of each
Combine basic gates into circuits
Describe the behavior of a gate using Boolean expressions, truth tables, and logic diagrams

## Slide 3: Definition
A gate is a device that performs a basic operation on electrical signals
Gates are combined into circuits to perform more complicated tasks
describing the behavior of gates and circuits by
  Boolean expressions
  logic diagrams
  truth tables

## Slide 4: Gates
six types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR

## Slide 5: NOT Gate
A NOT gate accepts one input value and produces one output value
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

## Slide 6: AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0

## Slide 7: OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1

## Slide 8: XOR Gate
XOR, or exclusive OR, gate
  An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise
  Note the difference between the XOR gate and the OR gate; they differ only in one input situation
  When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0

## Slide 9: NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively

## Slide 10: Review of Gate Processing
A NOT gate inverts its single input value
An AND gate produces 1 if both input values are 1
An OR gate produces 1 if one or the other or both input values are 1
An XOR gate produces 1 if one or the other (but not both) input values are 1
A NAND gate produces the opposite results of an AND gate
A NOR gate produces the opposite results of an OR gate

## Slide 11: Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1

## Slide 12: Circuits
Two general categories
  In a combinational circuit, the input values explicitly determine the output
  In a sequential circuit, the output is a function of the input values as well as the existing state of the circuit
As with gates, we can describe the operations of entire circuits using three notations
  Boolean expressions
  logic diagrams
  truth tables

## Slide 13: Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

## Slide 14: Combinational Circuits
Because there are three inputs to this circuit, eight rows are required to describe all possible input combinations
This same circuit using Boolean algebra:
(AB + AC)

## Slide 15: Now let’s go the other way; let’s take a Boolean expression and draw
Consider the following Boolean expression: A(B + C)
Now compare the final result column in this truth table to the truth table for the previous example
  They are identical

## Slide 16: Properties of Boolean Algebra

## Slide 17: Adders
At the digital logic level, addition is performed in binary
Addition operations are carried out by special circuits called, appropriately, adders
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10 in base two
A circuit that computes the sum of two bits and produces the correct carry bit is called a half adder

## Slide 18: Adders
Circuit diagram representing a half adder
Two Boolean expressions:
sum = A  B
carry = AB

## Slide 19: Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them

## Slide 20: Integrated Circuits

## Slide 21: CPU Chips
The most important integrated circuit in any computer is the Central Processing Unit, or CPU
Each CPU chip has a large number of pins through which essentially all communication in a computer system occurs

## Slide 22: The Von Neumann Model
Basic components
Instruction processing

## Slide 23: The von Neumann Model - 1
  Memory: holds the instructions and data
  Processing Unit: processes the information
  Input: external information into the memory
  Output: produces results for the user
  Control Unit: manages computer activity
Memory
Processing Unit
Input
Output
MAR
MDR
ALU
Register Set
Control Unit
PC
IR
*keyboard
*monitor

## Slide 24: The von Neumann Model - 2
Memory (RAM)
  Each location has an address and contents
  Address: set of bits that uniquely identify a memory location
    (eg. 20 bits gives an address space of 220 locations)
  Addressability (Byte vs. Word):
    The size of the memory location referenced by a given address

## Slide 25
Measuring Memory Capacity
Kilobyte: 210 bytes = 1024 bytes
  Example: 3 KB = 3 times1024 bytes
Megabyte: 220 bytes = 1,048,576 bytes
  Example: 3 MB = 3 times 1,048,576 bytes
Gigabyte: 230 bytes = 1,073,741,824 bytes
  Example: 3 GB = 3 times 1,073,741,824 bytes

## Slide 26: Data Communication Rates
Measurement units
  Bps: Bits per second
  Kbps: Kilo-bps (1,000 bps)
  Mbps: Mega-bps (1,000,000 bps)
  Gbps: Giga-bps (1,000,000,000 bps)
Bandwidth: Maximum available rate

## Slide 27: The von Neumann Model - 3
Processing Unit
  ALU (Arithmetic and Logic Unit)
    Generally operates on entire words of data
    Some also work on subsets of words (eg. bits and bytes)
  Registers:
    Small, fast “on-board” storage for words
    Close to the ALU (much faster access than RAM)
  Control Unit
    Program Counter (PC) or Instruction Pointer
        Holds the address of the next instruction to be executed
    Instruction Register (IR)
        Holds the instruction being executed
    The control unit coordinates all actions needed to execute the instruction

## Slide 30: Arithmetic/Logic Operations
Logic: AND, OR, XOR
Rotate and Shift: circular shift, logical shift, arithmetic shift
Arithmetic: add, subtract, multiply, divide

## Slide 31: Instructions
Instruction word: 16 bits
  Opcode
    defines (names) the instruction to be executed
    bits[15:12]: 4 bits allow 16 instructions
  Operands
    Registers: 8 registers (i.e. require 3 bits for addressing)
    Address parameters: Offset (9 bits) or Index (6 bits) (more later)
    Immediate value: 5 bits
Examples
  ADD DR, SR1, SR2 ; DR  (SR1) + (SR2)
  [15:12] [11:9] [8:6] [2:0] - Note: (Reg1) means “content of Reg1”
  LDR DR, BaseR, Offset ; DR  Mem[BaseR + Offset]
  [15:12] [11:9] [8:6] [5:0] - Note: Mem[loc] means “content of memory location loc”

## Slide 32: Instruction Cycle - 1
Six phases (steps)
  Fetch: load IR with instruction from memory
  Decode: determine action to take (which instructions)
  Evaluate address: compute memory address of operands, if any
  Fetch operands: read operands from memory or registers
  Execute: perform instruction
  Store results: write result to destination (register or memory)

## Slide 33: Instruction Cycle - 2
Fetch
  This actually takes several steps, represented here as “micro-instructions”, each of which can take a number of machine cycles to implement:
    MAR  (PC) ; use the value in PC to access memory
    MDR  Mem[MAR] ; read memory location to MDR
    IR  (MDR) ; move (MDR) to IR
    PC (PC) + 1 ; increment the value of PC
Decode
  A decoder reads the opcode bit pattern & sets up the next state of the machine to appropriately use the remaining bits of the instruction.

## Slide 34: Instruction Cycle - 3
Evaluate Address
  Computes the address of the memory location required to process the instruction (if any): e.g. the location from which to obtain a value.
  This is known as the Effective Address (EA).
Fetch Operands
  Obtains the source operand(s) (if any) either from Registers or from memory, i.e. from the EA calculated in the previous step.

## Slide 35: Instruction Cycle - 4
Execute
  Carries out the execution of the instruction - e.g. add two operands present at the input of the ALU
Store Result
  Writes the result (if any) to its designated destination, either register or memory (using the EA calculated earlier)
Start over …
  Recall that the PC was incremented already in the first step, so the next Fetch will bring back the next instruction - unless the instruction just executed changed the PC.

## Slide 36: Instruction Cycle - 5
Some instructions don't need all 6 phases
  If only using registers, skip Evaluate Address
  If only moving data, skip Execute
Control Instructions
  These change the sequence of instructions
    Branch
    Loop
    Function or procedure call
  Execute phase changes the content of the PC, so the next instruction will be out of sequence.