| Benha University Faculty of Engineering- Shoubra Electrical Engineering Department Second Year Communication |  | Mid-Term Exam Date: 29-04-2014 Test (2) Duration : 30 minutes |
| --- | --- | --- |

| Answer all the following question within the same paper | No. of questions:2 |
| --- | --- |
| Illustrate your answers with sketches when necessary. | Total Mark: 20 Marks |
| The exam. Consists of one page |  |

- (a) Draw a circuit used to record the characterstics of silicon diode, then draw the    expected output obtained by osccillscope. (5 marks)

(b) Show how to obtain a smooth dc signal from a full wave rectifier circuit. (5 marks)

- (a)  List some applications for Si-diode, zener diode, and LED. (6 marks).

(b) If the dc output voltage of  a half wave rectifier circuit is 0.318 volt, calculate the rms value of the input source. (2 marks).

(c) Draw the I-V characterstics of zener diode , compare it with that obtained in problem (1-a) (2 marks).

BOARD OF EXAMINERS

Dr Aly Mohamed Gomaa

| Benha University Faculty of Engineering- Shoubra Electrical Engineering Department Second Year Communication |  | Oral Exam Date: 29-04-2014 Test (2) Duration : 15 minutes |
| --- | --- | --- |

| Answer all the following question within the same paper | No. of questions:1 |
| --- | --- |
| Illustrate your answers with sketches when necessary. | Total Mark: 10 Marks |
| The exam. Consists of one page |  |

1- (a) for the circuit shown, show the function of this circuit then calculate the threshold voltage and current of the LED. (5 marks)

(b) re-calculate the requirements of (a) while replacing the LED by (i) Si-diode , (ii) Ge-diode, (iii) zener diode 4.7. (5 marks)

BOARD OF EXAMINERS

Dr Aly Mohamed Gomaa