## Slide 1: Electrical and Electronic Measurements
Part (2)
Signal Generators & Sensors
Lecture 5
د. باسم ممدوح الحلوانى

## Slide 2
Introduction to Sensors & Transducers
Sound is the generalized name given to “acoustic waves”.
Sound is basically a waveform of energy that is produced by some form of a mechanical vibration
These acoustic waves have frequencies ranging from just 1Hz up to 20 kHz
Sound requires a medium for transmission either through the air, a liquid, or a solid to be “heard”
Sound Transducers
Input-type Sound Transducers (Sensor) convert sound into and electrical signal
Microphone (mic)
Output-type Sound Transducers (actuators) convert the electrical signals back into sound
loudspeaker

## Slide 3
The Microphone Input Transducer
Sound Transducers
it produces an electrical analog output signal which is proportional to the “acoustic” sound wave acting upon its flexible diaphragm.
Many types are available such as Dynamic Moving-coil , condenser , Piezo-electric Crystal microphones
Dynamic Moving-coil Microphone Sound Transducer
It has a very small coil of thin wire suspended within the magnetic field of a permanent magnet.
As the sound wave hits the flexible diaphragm, the diaphragm moves back and forth in response to the sound pressure acting upon it
This causes the attached coil of wire to move within the magnetic field of the magnet.
The movement of the coil within the magnetic field causes a voltage to be induced in the coil as defined by Faraday’s law
The resultant output voltage signal from the coil is proportional to the pressure of the sound wave

## Slide 4
The Microphone Input Transducer
Sound Transducers
Condenser Microphone
Condenser means capacitor, the term condenser is actually obsolete but has stuck as the name for this type of microphone.
This Mic uses a capacitor to convert acoustical energy into electrical energy.
It requires power from a battery or external source.
The resulting audio signal is stronger signal than that from a dynamic.
Condensers also tend to be more sensitive and responsive than dynamics,
One of these plates is made of very light material and acts as the diaphragm.
The diaphragm vibrates when struck by sound waves, changing the distance between the two plates and therefore changing the capacitance

## Slide 5
The Microphone Input Transducer
Sound Transducers
Electret Condenser Microphone
The electret condenser mic uses a special type of capacitor which has a permanent voltage built in during manufacture. This is somewhat like a permanent magnet, in that it doesn't require any external power for operation.
An electret microphone is an omnidirectional microphone, which means it can capture sound from all directions.

## Slide 6
The Loudspeaker Output Transducer
Sound Transducers
Its job is to convert complex electrical analogue signals into sound waves being as close to the original input signal as possible.
Loudspeakers are available in all shapes, sizes and frequency ranges with the more common types being moving coil, electrostatic, isodynamic and piezoelectric.
Moving Coil Loudspeaker :
A coil of fine wire, called the “speech or voice coil”, is suspended within a very strong magnetic field, and is attached to a paper or Mylar cone, called a “diaphragm” which itself is suspended at its edges to a metal frame or chassis.
When an signal passes through the voice coil, an electro-magnetic field is produced which opposes the main permanent magnetic field around it and tries to push the coil in one direction or the other.
The principle of operation of the Moving Coil Loudspeaker is the exact opposite to that of the “Dynamic Microphone”
Since the coil is attached to the cone/diaphragm, the movement causes a disturbance in the air around it thus producing a sound

## Slide 7
Proximity Sensors
Types of proximity sensors
Non-Contact Sensors :
Optical
Ultrasonic
Inductive
Capacitive
Proximity sensors detect the presence or absence of objects using electromagnetic fields, light, and sound.
There are many types, each suited to specific applications and environments.
Contact Sensors (Mechanical)

## Slide 8
Proximity Sensors
Optical (Photoelectric) proximity Sensors
Photoelectric sensors are so versatile that they solve the bulk of problems
All photoelectric sensors consist of a few of basic components:
  An emitter light source (Light Emitting Diode, Infra-red LED, laser diode),
  A photodiode or phototransistor receiver to detect emitted light, and
  Supporting electronics designed to amplify the receiver signal.
Photoelectric proximity Sensors Configurations:
Through-beam
Retro-reflective
Diffuse

## Slide 9: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 10: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 11: Optical sensors (Through-beam)
Target
Transmitter
Receiver

## Slide 12: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 13: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 14: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 15: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 16: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 17: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 18: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 19: Optical sensors (Through-beam)
Transmitter
Receiver

## Slide 20: Optical sensors (Through-beam)
Target
Long sensing distance: up to 30 metres with some devices
Will detect all but very transparent materials
Must be accurately aligned
Transmitter
Receiver

## Slide 21: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Type : Retro reflective
Transmitter /Receiver

## Slide 22: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 23: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 24: Optical sensors (Retro-reflective)
Reflector (prismatic)
Target
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 25: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 26: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 27: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 28: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 29: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 30: Optical sensors (Retro-reflective)
Reflector (prismatic)
T
R
Transmitter /Receiver
Type : Retro reflective

## Slide 31: Optical sensors (Retro-reflective)
Reflector (prismatic)
Sensing distance : 1/2 to 1/3 of through-beam type
Not suitable for reflective or transparent targets
T
R
Type : Retro reflective
Transmitter /Receiver

## Slide 32: Optical sensors (Diffuse)
Target
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 33: Optical sensors (Diffuse)
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 34: Optical sensors (Diffuse)
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 35: Optical sensors (Diffuse)
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 36: Optical sensors (Diffuse)
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 37: Optical sensors (Diffuse)
T
R
Transmitter /Receiver
Type : Diffuse

## Slide 38: Optical sensors (Diffuse)
Transmitter /Receiver
Sensing distance: much less than reflex type, actual distance depends on colour and reflective nature of the surface
Larger targets result in longer sensing distances
Not suitable for dirty environments
T
R
Type : Diffuse

## Slide 39
Inductive proximity sensor
Coil inductance increases as iron / steel object (S ) gets closer
Capacitive proximity sensor
C1
C3
C2
Capacitance increases as metal object (P) gets closer because additional capacitance paths C2 & C3 are added and increase in value as the separation reduces. C1 is always present.
S
P
Non-contact Proximity sensors

## Slide 40: Non-contact Proximity sensors
Ultrasonic sensor utilize the reflection of high frequency (20KHz) sound waves to detect parts or distances to the parts.
In general, ultrasonic sensors are the best choice for transparent targets. They can detect a sheet of transparent plastic film as easily as a wooden pallet.
Different Colors has no effect
Ultrasonic (Sonar) sensors
The most common configurations are the same as in photoelectric sensing: through beam, retro-reflective, and diffuse versions.

## Slide 41: Non-contact Proximity sensors
Unlike IR sensors, sonars are slightly harder to deal with when it comes to multiple sensors.
Because of the wide cone, and how sound can reflect, they can interfere with each other quite easily.
Typically, you must allow a 50ms between each firing of a sonar sensors, to let the ping die off.
If you have multiple sensors, you can only ping one at a time, and must still obey this 50ms ring down time or have each sonar operating at a different sound frequency
Ultrasonic (Sonar) versus IR sensors
The primary difference is that sonar has a wide detection cone and longer range