## Slide 1: Electrical, Electronic and Digital Principles (EEDP)
Lecture 6
Amplifiers Classes
د. باسم ممدوح الحلوانى

## Slide 2
Classification Of Amplifiers
According to frequency capabilities.
According to coupling methods.
AF Amplifier are used to amplify the signals lying in the audio range ( i.e. 20 Hz to 20 kHz )
RF amplifiers are used to amplify signals having very high frequency.
Amplifiers are classified as audio amplifiers , radio frequency amplifiers
R-C coupled amplifiers,
Transformer coupled amplifiers
Direct Coupled

## Slide 3
Classification Of Amplifiers
According to use.
Amplify the input voltage, if possible with minimal current at the output.
The power gain of the voltage amplifier is low.
The main application is to strengthen the signal to make it less affected by noise and attenuation.
Ideal voltage amp. have infinite input impedance & zero output impedance.
Voltage amplifiers
Amplify the input power, if possible with minimal change in the output voltage
Power amp. are used in devices which require a large power across the loads.
In multi stage amplifiers, power amplification is made in the final stages
  Audio amplifiers and RF amplifiers use it to deliver sufficient power the load.
  Servo motor controllers use power it to drive the motors.
Power amplifiers

## Slide 4
Classification Of Amplifiers
 | Voltage amplifiers | Power amplifiers
current gain | low | high
Voltage gain | high | low
Heat dissipation | low | high
cooling mechanism | not required | required
Transistor Size | Small | Large to dissipate heat
Base Width | small | Wide to handle higher current
Beta | Usually high >100 | Low usually < 20

## Slide 5
(Mode of operation)

## Slide 9
Class B amplifier: When an amplifier is biased at cutoff so that it operates in the linear region for 180o of the input cycle and is in cutoff for 180o
Class AB amplifiers: are biased to conduct for slightly more than 180o
Both are more efficient than a class A amplifier;
A disadvantage of class B or class AB is that it is more difficult to implement the circuit in order to get a linear reproduction of the input waveform.
The term push-pull refers to a common type of class B or class AB amplifier circuit in which two transistors are used on alternating half-cycles to reproduce the input waveform at the output.

## Slide 10
The class B amplifier is biased at the cutoff point so that
It is brought out of cutoff and operates in its linear region when the input signal drives the transistor into conduction.
emitter-follower circuit
The Circuit only conducts for the positive half of the cycle.
Can not amplify the entire cycle

## Slide 11
To amplify the entire cycle, it is necessary to add a second class B amplifier that operates on the negative half of the cycle.
The combination of two class B amplifiers working together is called push-pull operation
There are two common approaches for using push-pull amplifiers to reproduce the entire waveform.
Transformer Coupling
The input transformer thus converts the input signal to two out-of-phase signals for the two npn transistors.
The output transformer combines the signals by permitting current in both directions, even though one transistor is always cut off.

## Slide 12
Complementary Symmetry Transistors
The figure shows one of the most popular types of push-pull class B amplifiers using two emitter-followers and both positive and negative power supplies.
This is a complementary amplifier because one emitter-follower uses an npn transistor and the other a pnp, which conduct on opposite alternations of the input cycle.

## Slide 13
When the dc base voltage is zero, both transistors are off and the input signal voltage must exceed VBE before a transistor conducts.
Because of this, there is a time interval between the positive and negative alternations of the input when neither transistor is conducting, as shown in Figure.
The resulting distortion in the output waveform is called crossover distortion.
Crossover Distortion

## Slide 14
To overcome crossover distortion, the biasing is adjusted to just overcome the VBE of the transistors
In class AB operation, the push-pull stages are biased into slight conduction, even when no input signal is present.
This can be done with a voltage-divider and diode arrangement, as shown
Biasing the Push-Pull Amplifier for Class AB Operation
Using equal values of R1 and R2 the positive and negative supply voltages forces the voltage at point A to equal 0 V and eliminates the need for an input coupling capacitor.
When the diode characteristics of D1 and D2 are closely matched to the characteristics of the transistor BE junctions, the current in the diodes and the current in the transistors are the same; ((current mirror.))
The diode current will be the same as ICQ

## Slide 15
AC Operation
Biasing the Push-Pull Amplifier for Class AB Operation
The Q-point is slightly above cutoff. (In a true class B amplifier, the Q-point is at cutoff.)
The ac cutoff voltage is at VCC
The ac saturation current is:
In class A , the Q-point is near the middle and there is significant current in the transistors even with no signal.
In class B , when there is no signal, the transistors have only a very small current and therefore dissipate very little power.
Thus, the efficiency of a class B amplifier can be much higher than a class A amplifier.

## Slide 16
The circuit operation is the same as that described previously, except the bias is set to force the output emitter voltage to be

## Slide 17
Maximum Output Power
DC Input Power
Efficiency

## Slide 18
Class C amplifiers are biased so that conduction occurs for much less than 180o
Class C amplifiers are more efficient than either class A , B, or AB
Class C amplifiers
The output amplitude is a nonlinear function of the input, so class C amplifiers are not used for linear amplification.
They are generally used in radio frequency (RF) applications, including resonance circuits
Basic Class C Operation
A class C amplifier is normally operated with a resonant circuit load, so the resistive load is used only for the purpose of illustrating the concept.
The ac source voltage has a peak value that exceeds the barrier potential of the base-emitter junction for a short time near the positive peak of each cycle,

## Slide 19
Class C amplifiers
Basic Class C Operation
During this short interval, the transistor is turned on.
The power dissipation of the transistor in a class C amplifier is low because it is on for only a small percentage of the input cycle
The power dissipation during the on time is
The power dissipation averaged over the entire cycle is
Check EXAMPLE 7–7 (Floyde)

## Slide 20
Tuned Class C Operation
Because the collector voltage (output) is not a replica of the input, the resistively loaded class C amplifier alone is of no value in linear applications.
It is therefore necessary to use a class C amplifier with a parallel resonant circuit (tank), as shown
The short pulse of collector current on each cycle of the input initiates and sustains the oscillation of the tank circuit so that an output sinusoidal voltage is produced