## Slide 1
Lecture 09 Field Effect Transistors (2)
Prepared By
Dr. Eng. Sherif Hekal
Assistant Professor, CCE department
CCE201: Solid State Electronic Devices
EEC223: Electronics (1)

## Slide 2: Introduction
IN THIS LECTURE WE WILL LEARN
  How the transistor can be used to make an amplifier, and how it can be used as a switch in digital circuits.
  How to obtain linear amplification from the fundamentally nonlinear MOS transistor.

## Slide 3: 3. MOSFET Circuits at DC
We move on to discuss how MOSFET’s behave in dc circuits.
We will neglect the effects of channel length modulation (assuming l = 0).
We will work in terms of overdrive voltage (vOV), which reduces need to distinguish between PMOS and NMOS.
DC

## Slide 4: Example 1: NMOS Transistor
Problem Statement: Design the circuit of Figure 21, that is, determine the values of RD and RS – so that the transistor operates at ID = 0.4mA and VD = +0.5V. The NMOS transistor has Vt = 0.7V, mnCox = 100mA/V2, L = 1mm, and W = 32mm. Neglect the channel-length modulation effect (i. e. assume that l = 0).

## Slide 5: Example 1 - Sol

## Slide 6: Example 2: MOSFET
Problem Statement: Design the circuit in Figure to establish a drain voltage of 0.1V. What is the effective resistance between drain and source at this operating point? Let Vtn = 1V and k’n(W/L) = 1mA/V2.

## Slide 7: Example 2 - Sol

## Slide 8: Example 3: MOSFET
Problem Statement: Analyze the circuit shown in Figure(a) below to determine the voltages at all nodes and the current through all branches. Let Vtn = 1V and k’n(W/L) = 1mA/V2. Neglect the channel-length modulation effect (i.e. assume l = 0).

## Slide 9: Example 3 - Sol
With this positive voltage at the gate, the NMOS transistor will be turned on. We do not know, however, whether the transistor will be operating in the saturation region or in the triode region. We shall assume saturation-region operation, solve the problem, and then check the validity of our assumption. Obviously, if our assumption turns out not to be valid, we will have to solve the problem again for triode-region operation.
Refer to Fig. (b). Since the voltage at the gate is 5 V and the voltage at the source is

## Slide 10: Example 3 – Sol, cont.

## Slide 11: 4.1. Obtaining a Voltage Amplifier
Previously, we learned that voltage controlled current source (VCCS) can serve as transconductance amplifier.
Q: How can we translate current output to voltage?
  A: Measure voltage drop across load resistor.
example of transconductance amplifier
(Eq. 8)

## Slide 12: 4.2. Voltage Transfer Characteristic
voltage transfer characteristics (VTC) – plot of out voltage vs. input
three regions exist in VTC
  vGS < Vt  cut off FET
    vOV = vGS – Vt < 0
    ID = 0
    vDS ??? vOV
    vout = vDD
  Vt < vGS < vDS + Vt  saturation
    vOV = vGS – Vt > 0
    ID = ½ kn(vGS – Vt)2
    vDS >> vOV
    vout = VDD – IDRD
  vDS + Vt < vGS < VDD  triode
    vOV = vGS – Vt > 0
    ID = kn(vGS – Vt – vDS)vDS
    vDS > vOV
    vout = VDD – IDRD
Figure 11: (b) the voltage transfer characteristic (VTC) of the amplifier from previous slide

## Slide 13: 4.2. Voltage Transfer Characteristic
Q: What observations may be drawn?
  A: Cutoff MOSFET represents transistor blocking, cutoff AMP represents vout = 0
  A: As vGS increases…
    vDS (effectively) decreases
    iD increases
    vout decreases nonlinearly
    gain (G) decreases
Figure 11: (b) the voltage transfer characteristic (VTC) of the amplifier from previous slide

## Slide 14: 4.3. Biasing the MOSFET to Obtain Linear Amplification
Q: How can we linearize VTC?
  A: Appropriate biasing technique
  A: Dc voltage vGS is selected to obtain operation at point Q on segment AB
Q: How do we choose vGS?
  A: Will discuss shortly…
Figure 12: biasing the MOSFET amplifier at point Q located on segment AB of VTC
(Eq. 9)

## Slide 15: 4.3. Biasing the MOSFET to Obtain Linear Amplification
bias point / dc operating pt. (Q) – point of linearization for MOSFET
  Also known as quiescent point.
Q: How will Q help us?
  A: Because VTC is linear near Q, we may perform linear amplification of signal << VGSQ
Figure 12: biasing the MOSFET amplifier at point Q located on segment AB of VTC
(Eq. 9)

## Slide 16: 4.3. Biasing the MOSFET to Obtain Linear Amplification
Q: How is linear gain achieved?
  step #1: Bias MOSFET with dc voltage VGS as defined by (Eq. 10)
  step #2: Superimpose amplifier input (vgs) upon VGS.
  step #3: Resultant vds should be linearly proportional to small-signal component vgs.

## Slide 17: Q: How is linear gain achieved?
Figure 13: The MOSFET amplifier with a small time-varying signal vgs(t) superimposed on the dc bias voltage vGS. The MOSFET operates on a short almost-linear segment of the VTC around the bias point Q and provides an output voltage vds = Avvgs
As long as vgs(t) is small, its effect on vDS(t) will be linear – facilitating linear amplification.

## Slide 18: Q: How is linear gain achieved?
(Eq. 10)
step #4: Note if vgs is small, output vds will be nearly linearly proportional to it.
  Slope will be constant.

## Slide 19: 4.4. Small-Signal Voltage Gain
Q: What observations can be made about voltage gain?
  A: Gain is negative.
  A: Gain is proportional to:
    load resistance (RD)
    transistor conductance parameter (kn)
    overdrive voltage (vOV)
(Eq. 10)

## Slide 20: 4.4. Small-Signal Gain
Equation (11) is another version of (10).
It demonstrates that gain is ratio of:
  voltage drop across RD
  half of over voltage
(Eq. 11)

## Slide 21: Example 4: MOSFET Amplifier
Problem Statement: Consider the amplifier circuit shown in Figure 29. The transistor is specified to have Vt = 0.4V, k’n = 0.4mA/V2, W/L = 10, and l = 0. Also, let VDD = 1.8V, RD = 17.5kOhms, and VGS = 0.6V.
Q(a): For vgs = 0 (and hence vds = 0), find VOV, ID, VDS, and Av.
Q(b): What is the maximum symmetrical signal swing allowed at the drain? Hence, find the maximum allowable amplitude of a sinusoidal vgs.

## Slide 22: Example 4 – Sol
Since is greater than , the transistor is indeed operating in saturation. The voltage gain is given by

## Slide 23: Example 4 – Sol, Cont.

## Slide 24: 4.5. Determining the VTC via Graphical Analysis
Graphical method for determining VTC is shown in Figure 31
Rarely used in practice, b/c difficult to draw vi-relationship.
Based on observation that, for each value of vGS, circuit will operate at intersection of iD and vDS.
Figure 14: Graphical construction to determine the voltage transfer characteristic of the amplifier in Fig. 13.
note: that slope of load line is dependent on -1/RD
(Eq. 12)

## Slide 25: 4.5. Determining the VTC via Graphical Analysis
point A – where vGS = Vt
point Q – where MOSFET may be biased for amplifier operation
  vGS = VGS, vDS = VDS
point B – where MOSFET leaves saturation / enters triode
point C – where MOSFET is deep in triode region and vGS = VDD
Points A (open) and C (closed) are suitable for switch applications
Point Q is suitable for amplifier applications

## Slide 26: 4.5. Determining the VTC via Graphical Analysis
Figure 15: Operation of the MOSFET in Figure 13 as a switch: (a) Open, corresponding to point A in Figure 14; (b) Closed, corresponding to point C in Figure 14. The closure resistance is approximately equal to rDS because VDS is usually very small.

## Slide 27: 5. Small-Signal Operation and Models
Previously it was stated that linear amplification may be obtained from MOSFET via…
  Operation in saturation region
  Utilization of small-input
This section will explore small-signal operation in detail
  Note the conceptual amplifier circuit to right
Figure 16: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.
dc bias voltage
output voltage
input voltage to be amplified

## Slide 28: 5.1. The DC Bias Point
Q: How is dc bias current ID defined?
Figure 16: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.

## Slide 29: 5.2. The Signal Current in the Drain Terminal
Q: What is effect of vgs on iD?
  step #1: Define vGS as in (5.42).
  step #2: Define iD, separate terms as function of VGS and vgs

## Slide 30: Q: What is effect of vgs on iD?
step #3: Classify terms.
  dc bias current (ID).
  linear gain – is desirable.
  nonlinear distortion – is undesirable, because rep. distortion.
Note that to minimize nonlinear distortion, vgs should be kept small.
½knvgs2 << kn(VGS-Vt)vgs
vgs << 2(VGS-Vt)
vgs << 2vOV

## Slide 31: Q: What is effect of vgs on iD?
step #4: Adapt (5.43) for small-signal condition.
  If vgs << 2vOV , neglect distortion.

## Slide 32
Figure 17: Small-signal operation of the MOSFET amplifier.

## Slide 33: 5.3. The Voltage Gain
Q: How is voltage gain (Av) defined?
  step #1: Define vDS for circuit of Figure 34 using KVL.
Figure 16: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.

## Slide 34: Q: How is voltage gain (Av) defined?
step #2: Isolate vds component of vDS.
step #3: Solve for gain (Av).
Figure 16: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.
(Eq. 13)

## Slide 35: 5.3. The Voltage Gain
Output signal is shifted from input by 180O.
Input signal vgs << 2(VGS – Vt).
Operation should remain in MOSFET saturation region
  vDS > vGS – Vt (legroom)
  vDS < VDD (headroom)
Figure 18: Total instantaneous voltage vGS and vDS for the circuit in Figure 5.34.

## Slide 36: 5.5. Small-Signal Equivalent Models
From signal POV, FET behaves as VCCS.
  Accepts vgs between gate and source
  Provides current (iD) at drain
  Input resistance is high
    b/c gate terminal draws iG = 0
  Output resistance is high
Figure 19: Small-signal models for the MOSFET: (a) neglecting the dependence of iD on vDS in saturation (the channel-length modulation effect) and (b) including the effect of channel length modulation

## Slide 37: 5.5. Small-Signal Equivalent Models
Figure 19: Small-signal models for the MOSFET: (a) neglecting the dependence of iD on vDS in saturation (the channel-length modulation effect) and (b) including the effect of channel length modulation
Note that this resistor (ro) takes on value 10kOhm to 1MOhm and represents channel-length modulation.

## Slide 38: More Observations
Model (b) is more accurate than model (a)
ro = VA / ID
Small signal parameters (gm, ro) both depend on dc bias point
If channel-length modulation is considered, (Eq. 14) becomes (Eq. 15).
(Eq. 14)
(Eq. 15)

## Slide 39: 5.6: The Transconductance gm
In summary, there are three relationships for determining gm
These relationships are dependent on three design parameters:
  W/L, VOV, ID

## Slide 40: Example 5: MOSFET Amplifier
Problem Statement: Figure 39 shows a discrete common-source MOSFET amplifier utilizing a drain-to-gate resistance RG for biasing purposes. The input signal vI is coupled to the gate via a large capacitor, and the output signal at the drain is coupled to the load resistance RL via another large capacitor. The transistor has Vt = 1.5V, k’n(W/L) = 0.25mA/V2, and VA = 50V. Assume the coupling capacitors to be sufficiently large so as to act as short circuits at the signal-frequencies of interest.
Q: We wish to analyze this amplifier circuit to determine its (a) small-signal voltage gain, its (b) input resistance, and the largest allowable input signal.

## Slide 41
Figure 20: Example 5 amplifier circuit.
note: capacitors block dc signals completely, but have no effect on small-signal

## Slide 42: Example 5 – Sol
We first determine the dc operating point.
1- DC analysis: as shown in the figure
We note that since , the dc voltage drop across will be zero, and
Solving the resulting quadratic equation in and discarding the root that is not physically meaningful yields the solution

## Slide 43: Example 5 – Sol, Cont.
Next we proceed with the small-signal analysis of the amplifier.
The values of the transistor small-signal parameters gm and ro can be determined by using the dc bias quantities found above,

## Slide 44: Example 5 – Sol, Cont.
Toward that end we simplify the circuit by combining the three parallel resistances , , and in a single resistance ,
 (1)
 (2)

## Slide 45: Example 5 – Sol, Cont.
Substituting for from Eq. (2) into Eq. (1) results in the following expression for the voltage gain:
To obtain the input resistance, we substitute in Eq. (1) for , then use to obtain
which is still very large.

## Slide 46: Example 5 – Sol, Cont.

## Slide 48: Summary
The enhancement-type MOSFET is current the most widely used semiconductor device. It is the basis of CMOS technology, which is the most popular IC fabrication technology at this time. CMOS provides both n-channel (NMOS) and p-channel (PMOS) transistors, which increases design flexibility. The minimum MOSFET channel length achievable with a given CMOS process is used to characterize the process
The overdrive voltage |VOV| = |VGS| - |Vt| is the key quantity that governs the operation of the MOSFET. For amplifier applications, the MOSFET must operate in the saturation region.

## Slide 49: Summary
In saturation, iD shows some linear dependence on vDS as a result of the change in channel length. This channel-length modulation phenomenon becomes more pronounced as L decreases. It is modeled by ascribing an output resistance ro = |VA|/ID to the MOSFET model. Although the effect of ro on the operation of discrete-circuit MOS amplifiers is small, that is not the case in IC amplifiers.
The essence of the use of MOSFET as an amplifier is that in saturation vGS controls iD in the manner of a voltage-controller current source. When the device is dc biased in the saturation region, a small-signal input (vgs) may be amplified linearly.
In cases where a resistance is connected in series with the source lead of the MOSFET, the T model is the most convenient to use.