## Slide 1: Lecture 03 Semiconductor Physics
Prepared By
Dr. Eng. Sherif Hekal
Assistant Professor, CCE department

## Slide 2: ILOS
In this section, we will learn:
  The basic properties of semiconductors and, in particular, silicone – the material used to make most modern electronic circuits.
  How doping a pure silicon crystal dramatically changes electrical conductivity – the fundamental idea in underlying the use of semiconductors in the implementation of electronic devices.
  The two mechanisms by which current flows in semiconductors – drift and diffusion charge carriers.
  The structure and operation of the pn junction – a basic semiconductor structure that implements the diode and plays a dominant role in semiconductors.

## Slide 3: Agenda
Current Flow in Semiconductors
The pn Junction with Open-Circuit Terminals (Equilibrium)
The pn Junction with Applied Voltage
Capacitive Effects in the pn Junction

## Slide 4: Intrinsic Semiconductors
Q: Why can thermal generation not be used to affect meaningful current conduction?
  A: Silicon crystal structure described previously is not sufficiently conductive at room temperature.
    Additionally, a dependence on temperature is not desirable.
Q: How can this “problem” be fixed?
  A: doping
doping – is the intentional introduction of impurities into an extremely pure (intrinsic) semiconductor for the purpose changing carrier concentrations.
Notes: Doping is placing pure crystalline silicon in an environment with a gas containing the desired impurity and elevating the temperature so that high energy atoms penetrate the silicon and randomly bump out some silicon atoms.

## Slide 5: Doped Semiconductors
p-type semiconductor
  Silicon is doped with element having a valence of 3.
  To increase the concentration of holes (p).
  One example is boron, which is an acceptor.
n-type semiconductor
  Silicon is doped with element having a valence of 5.
  To increase the concentration of free electrons (n).
  One example is phosophorus, which is a donor.
A semiconductor material that has been subjected to the doping process is called an extrinsic material.
Notes: Look at the periodic table of the elements. The columns correspond to the number of valence electrons.
The intrinsic silicon crystal described above has equal concentrations of free electrons and holes, generated by thermal generation. These concentrations are far too small for silicon to conduct appreciable current at room temperature. Also, the carrier concentrations and hence the conductivity are strong functions of temperature, not a desirable property in an electronic device. Fortunately, a method was developed to change the carrier concentration in a
semiconductor crystal substantially and in a precisely controlled manner. This process is known as doping, and the resulting silicon is referred to as doped silicon.

## Slide 6: Doped Semiconductors
p-type semiconductor
n-type semiconductor

## Slide 7
p-type
N-type

## Slide 8: Doped Semiconductors
p-type doped semiconductor
  If NA is much greater than ni …
    concentration of acceptor atoms is NA
  Then the concentration of holes in the p-type is defined as below.

## Slide 9: Doped Semiconductors
n-type doped semiconductor
  If ND is much greater than ni …
    concentration of donor atoms is ND
  Then the concentration of electrons in the n-type is defined as below.
The key here is that number of free electrons (conductivity) is dependent on doping concentration, not temperature…

## Slide 10: Doped Semiconductors
p-type semiconductor
  Q: How can one find the concentration?
    A: Use the formula to right, adapted for the p-type semiconductor.
Notes: These are “densities”

## Slide 11: Doped Semiconductors
n-type semiconductor
  Q: How can one find the concentration?
    A: Use the formula to right, adapted for the n-type semiconductor.

## Slide 12: Doped Semiconductors
p-type semiconductor
  np will have the same dependence on temperature as ni2
  the concentration of holes (pn) will be much larger than free electrons
  holes are the majority charge carriers
  free electrons are the minority charge carrier
n-type semiconductor
  pn will have the same dependence on temperature as ni2
  the concentration of free electrons (nn) will be much larger than holes
  electrons are the majority charge carriers
  holes are the minority charge carrier

## Slide 13: Doped Semiconductors
It should be emphasized that a piece of n-type or p-type silicon is electrically neutral; the charge of the majority free carriers (electrons in the n-type and holes in the p-type silicon) are neutralized by the bound charges associated with the impurity atoms.
Let
no : thermal-equilibrium concentration of electrons
po : thermal-equilibrium concentration of holes
Nd : concentration of donor atoms
Na : concentration of acceptor atoms
Nd+ : concentration of positively charged donors (ionized donors)
Na- : concentration of negatively charged acceptors (ionized acceptors)

## Slide 14: Doped Semiconductors
by the charge neutrality condition, n0 + Na- = p0 + Nd+
At equilibrium, the product of the majority and minority carrier concentration is a constant, and this is mathematically expressed by the Law of Mass Action.

## Slide 15: Example 2: Doped Semiconductor
Consider an n-type silicon for which the dopant concentration is ND = 1017/cm3. Find the electron and hole concentrations at T = 300K.
Solution
The concentration of the majority electrons is
The concentration of the minority holes is
In Example 1, we found that at T = 300 K,
. Thus,
Observe that and that is vastly higher than .

## Slide 16: Example 3 : Doped Semiconductor
For a silicon crystal doped with boron, what must NA be if at T = 300 K the electron concentration drops below the intrinsic level by a factor of 106?

## Slide 17: Current Flow in Semiconductors

## Slide 18: 1. Drift Current
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are attracted.
Q: How is the velocity of these carriers defined?
There are two distinctly different mechanisms for the movement of charge carriers and hence for current flow in semiconductors: drift and diffusion.
Notes: The electric field is determined by applied voltages (divided by the distance between the voltages)

## Slide 19: 1. Drift Current
.E (volts / cm)
.mp (cm2/Vs) = 480 for silicon
.mn (cm2/Vs) = 1350 for silicon
note that electrons move with velocity 2.5 times higher than holes
Notes: The carriers move slowly, not at the speed of light, but signals can move at near the speed of light.
hole mobility: It represents the degree of ease by which holes move through the silicon crystal in response to the electrical field E. vn-drift where the result is negative because the electrons move in the direction opposite to E.
The mobility is proportional to the carrier relaxation time and inversely proportional to the carrier effective mass. The electron mobilty is often greater than hole mobility because quite often, the electron effective mass is smaller than hole effective mass.

## Slide 20: 3.3.1. Drift Current
Q: What happens when an electrical field (E) is applied to a semiconductor crystal?
  A: Holes are accelerated in the direction of E, free electrons are repelled.
Q: How is the velocity of these holes defined?
An electric field E established in a bar of silicon causes the holes to drift in the direction of E and the free electrons to drift in the opposite direction. Both the hole and electron drift currents are in the direction of E.
HOLES
ELECTRONS

## Slide 21: Current and Current Density
Current density may be related to the velocity of volume charge density at a point.
Consider the element of charge , as shown in Figure (a).

## Slide 22: Current and Current Density
To simplify the explanation, assume that the charge element is oriented to the x-axis and has only an x component of velocity .
If the charge element moved a distance in the time interval , as indicated in Figure (b), the resulting current will be
Where represents the x component of the velocity v. In terms of current density,
we find
and in general

## Slide 23: 1. Drift Current
Assume that, for the single-crystal silicon bar on previous slide, the concentration of holes is defined as p and electrons as n.
Q: What is the current component attributed to the flow of holes (not electrons)?

## Slide 24: 1. Drift Current
step #1: Consider a plane perpendicular to the x direction.
step #2: Define the hole charge that crosses this plane.

## Slide 25: 1. Drift Current
step #3: Substitute in mpE.
step #4: Define current density as Jp = Ip / A.
PART A: What is the current component attributed to the flow of holes (not electrons)?

## Slide 26: 1. Drift Current
Q: What is the current component attributed to the flow of electrons (not holes)?
  A: to the right…
Q: How is total drift current defined?
  A: to the right…

## Slide 27: 1. Drift Current

## Slide 28: 1. Drift Current
conductivity (s.) – relates current density (J) and electrical field (E)
resistivity (r.) – relates current density (J) and electrical field (E)

## Slide 29: Example 4: Drift current
Q(a): Find the resistivity of intrinsic silicon using following values – mn = 1350cm2/Vs, mp = 480cm2/Vs, ni = 1.5x1010/cm3.
Q(b): Find the resistivity of p-type silicon with NA = 1016/cm2 and using the following values – mn = 1110cm2/Vs, mp = 400cm2/Vs, ni = 1.5x1010/cm3
note that doping reduces carrier mobility

## Slide 30: Example 5: Drift current
p = n = ni = 1.5 × 1010 ⁄ cm3
(a) For intrinsic silicon,
(b) For the p-type silicon
Notes: Observe that the resistivity of the p-type silicon is determined almost entirely by the doping concentration.
Also observe that doping the silicon reduces its resistivity by a factor of about , a truly remarkable change.

## Slide 31: Note…
for intrinsic semiconductor – number of free electrons is ni and number of holes is pi
for p-type doped semiconductor – number of free electrons is np and number of holes is pp
for n-type doped semiconductor – number of free electrons is nn and number of holes is pn
majority charge carriers
minority charge carriers

## Slide 32: Example 6: Drift current
A uniform bar of n-type silicon of 2 μm length has a voltage of 1 V applied across it. If and .s, find (a) the electron drift velocity, (b) the time it takes an electron to cross the 2-μm length, (c) the drift-current density, and (d) the drift current in the case the silicon bar has a cross sectional area of .

## Slide 33: Example 6: Drift current, contd.
A
length
c. The current density is given by

## Slide 34: 2. Diffusion Current
carrier diffusion – is the flow of charge carriers from area of high concentration to low concentration.
  It requires non-uniform distribution of carriers.
diffusion current – is the current flow that results from diffusion.
Notes: Such a diffusion process is like that observed if one drops a few ink drops in a water-filled tank. The diffusion of charge carriers gives rise to a net flow of charge, or diffusion current.

## Slide 35: 2. Diffusion Current
Take the following example…
  inject holes – By some unspecified process, one injects holes in to the left side of a silicon bar.
  concentration profile arises – Because of this continuous hole inject, a concentration profile arises.
  diffusion occurs – Because of this concentration gradient, holes will flow from left to right.
inject holes
concentration profile arises
diffusion occurs
Notes: The magnitude of the current at any point is proportional to
the slope of the concentration profile, or the concentration gradient, at that point,

## Slide 36: 2. Diffusion Current
Q: How is diffusion current defined?
Unit: A/cm2
Notes: Note that the gradient dp(x)/dx is negative, resulting in a positive current in the x direction, as should be expected.
Observe that a negative (dn/dx) gives rise to a negative current, a result of the convention that the positive direction of current
is taken to be that of the flow of positive charge (and opposite to that of the flow of negative charge).

## Slide 37: 2. Diffusion Current
Observe that a negative (dn/dx) gives rise to a negative current, a result of the convention that the positive direction of current is taken to be that of the flow of positive charge (and opposite to that of the flow of negative charge).
Notes: At this point the reader is probably wondering where the diffusion current in the silicon bar in Fig. 3.6(a) goes. A good question as we are not showing how the right-side end of the bar is connected to the rest of the circuit. We will address this and related questions in detail in our discussion of the pn junction in later sections.

## Slide 38: Example 7: Diffusion current
Consider a bar of silicon in which a hole concentration p(x) described below is established.
Q(a): Find the hole-current density Jp at x = 0.
Q(b): Find current Ip.
  Note the following parameters: p0 = 1016/cm3, Lp = 1mm, A = 100mm2
Notes: A = cross-sectional area of the bar

## Slide 39: Example 7: Diffusion current, contd.

## Slide 40: 3. Relationship Between D and m.?
Q: What is the relationship between diffusion constant (D) and mobility (m)?
  A: thermal voltage (VT)
Q: What is this value?
  A: at T = 300K, VT = 25.9mV
known as Einstein Relationship

## Slide 41: Summary of Semiconductor currents
drift current density (Jdrift)
  affected by – an electric field (E).
diffusion current density (Jdiff)
  affected by – concentration gradient in free electrons and holes.

## Slide 42: 4. The pn Junction with Open-Circuit Terminals 4.1. Physical Structure
pn junction structure
  p-type semiconductor
  n-type semiconductor
  metal contact for connection
Simplified physical structure of the pn junction. As the pn junction implements the junction diode, its terminals are labeled anode and cathode.
Notes: This is a semiconductor diode. Anode and cathode are old terms from vacuum tube circuits.
In actual practice, both the p and n regions are part of the same silicon crystal; that is, the pn junction is formed within a single silicon crystal by creating regions of different dopings (p and n regions).
Having learned important semiconductor concepts, we are now ready to consider our first practical semiconductor structure—the pn junction. As mentioned previously, the pn junction implements the diode (Chapter 4) and plays the dominant role in the structure and operation of the bipolar junction transistor (BJT). As well, understanding pn junctions is very important to the study of the MOSFET operation

## Slide 43: 4.2. Operation with Open-Circuit Terminals
Q: What is state of pn junction with open-circuit terminals?
A: Read the below…
  p-type material contains majority of holes
    these holes are neutralized by equal amount of bound negative charge
  n-type material contains majority of free electrons
    these electrons are neutralized by equal amount of bound positive charge

## Slide 44: 4.2. Operation with Open-Circuit Terminals
bound charge
  charge of opposite polarity to free electrons / holes of a given material
  neutralizes the electrical charge of these majority carriers
  does not affect concentration gradients
Figure: The pn junction with no applied voltage (open-circuited terminals).
positive bound charges
negative bound charges
p-type
n-type
free electrons
free holes
Notes: The Diffusion Current ID

## Slide 45: 4.2. Operation with Open-Circuit Terminals
Q: What happens when a pn-junction is newly formed – aka. when the p-type and n-type semiconductors first touch one another?
  A: See following slides…

## Slide 46: Step #1: The p-type and n-type semiconductors are joined at the junction.
Figure: The pn junction with no applied voltage (open-circuited terminals).
n-type semiconductor filled with free electrons
p-type semiconductor filled with holes
junction
Notes: The distribution of carriers is approximately uniform (but random).

## Slide 47: Step #2: Diffusion begins. Those free electrons and holes which are closest to the junction will recombine and, essentially, eliminate one another.
Figure: The pn junction with no applied voltage (open-circuited terminals).
p-type
n-type

## Slide 48: Step #3: The depletion region begins to form – as diffusion occurs and free electrons recombine with holes.
The depletion region is filled with “uncovered” bound charges – who have lost the majority carriers to which they were linked.
Figure: The pn junction with no applied voltage (open-circuited terminals).
p-type
n-type
Notes: Now the distribution near the junction is not uniform due to recombination.

## Slide 49: Step #4: The “uncovered” bound charges affect a voltage differential across the depletion region. The magnitude of this barrier voltage (V0) differential grows, as diffusion continues.
voltage potential
location (x)
barrier voltage (Vo)
No voltage differential exists across regions of the pn-junction outside of the depletion region because of the neutralizing effect of positive and negative bound charges.
p-type
n-type
Notes: Barrier in that it resists current flow.

## Slide 50: Step #5: The barrier voltage (V0) is an electric field whose polarity opposes the direction of diffusion current (ID). As the magnitude of V0 increases, the magnitude of ID decreases.
Figure: The pn junction with no applied voltage (open-circuited terminals).
diffusion current (ID)
drift current (IS)
p-type
n-type

## Slide 51: Step #6: Equilibrium is reached, and diffusion ceases, once the magnitudes of diffusion and drift currents equal one another – resulting in no net flow.
diffusion current (ID)
drift current (IS)
Once equilibrium is achieved, no net current flow exists (Inet = ID – IS) within the pn-junction while under open-circuit condition.
p-type
n-type
depletion region

## Slide 52: 4.2. Operation with Open-Circuit Terminals
pn-junction built-in voltage (V0) – is the equilibrium value of barrier voltage.
  It is defined to the right.
  Generally, it takes on a value between 0.6 and 0.9V for silicon at room temperature.
  This voltage is applied across depletion region, not terminals of pn junction.
    Power cannot be drawn from V0.
Notes: And the terminal voltage needs to exceed the barrier voltage before appreciable current flows.

## Slide 53: Report 1

## Slide 54: The Drift Current IS and Equilibrium
In addition to majority-carrier diffusion current (ID), a component of current due to minority carrier drift exists (IS).
Specifically, some of the thermally generated holes in the p-type and n-type materials move toward and reach the edge of the depletion region.
Therefore, they experience the electric field (V0) in the depletion region and are swept across it.
  Unlike diffusion current, the polarity of V0 reinforces this drift current.
Notes: Isis the leakage current that flows when the diode is reverse biased.

## Slide 55: 4.2. Operation with Open-Circuit Terminals
Because these holes and free electrons are produced by thermal energy, IS is heavily dependent on temperature
Any depletion-layer voltage, regardless of how small, will cause the transition across junction. Therefore IS is independent of V0.
drift current (IS) – is the movement of these minority carriers.
  aka. electrons from p-side to n-side of the junction

## Slide 56: Note that the magnitude of drift current (IS) is unaffected by level of diffusion and / or V0. It will be, however, affected by temperature.
Figure: The pn junction with no applied voltage (open-circuited terminals).
diffusion current (ID)
drift current (IS)

## Slide 57: 4.2. Operation with Open-Circuit Terminals
Q: How is the charge stored in both sides of the depletion region defined?
  A: Refer to equations to right. Note that these values should equal one another.

## Slide 58: 4.2. Operation with Open-Circuit Terminals
Q: What information can be derived from this equality?
  A: In reality, the depletion region exists almost entirely on one side of the pn-junction – due to great disparity between NA > ND.

## Slide 59: 4.2. Operation with Open-Circuit Terminals
Note that both xp and xn may be defined in terms of the depletion region width (W).

## Slide 60: 4.2. Operation with Open-Circuit Terminals
Note, also, the charge on either side of the depletion region may be calculated via (3.29) and (3.30).

## Slide 61: 4.2. Operation with Open-Circuit Terminals
Q: What has been learned about the pn-junction?
  A: composition
    The pn junction is composed of two silicon-based semiconductors, one doped to be p-type and the other n-type.
  A: majority carriers
    Are generated by doping.
    Holes are present on p-side, free electrons are present on n-side.

## Slide 62: 3.4.2. Operation with Open-Circuit Terminals
Q: What has been learned about the pn-junction?
  A: bound charges
    Charge of majority carriers are neutralized electrically by bound charges.
  A: diffusion current ID
    Those majority carriers close to the junction will diffuse across, resulting in their elimination.

## Slide 63: 4.2. Operation with Open-Circuit Terminals
Q: What has been learned about the pn-junction?
  A: depletion region
    As these carriers disappear, they release bound charges and effect a voltage differential V0.
  A: depletion-layer voltage
    As diffusion continues, the depletion layer voltage (V0) grows, making diffusion more difficult and eventually bringing it to halt.

## Slide 64: 4.2. Operation with Open-Circuit Terminals
Q: What has been learned about the pn-junction?
  A: minority carriers
    Are generated thermally.
    Free electrons are present on p-side, holes are present on n-side.
  A: drift current IS
    The depletion-layer voltage (V0) facilitates the flow of minority carriers to opposite side.
  A: open circuit equilibrium ID = IS

## Slide 65: 5. The pn Junction with an Applied Voltage 5.1. Qualitative Description of Junction Operation
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
Notes: This determines the Diode V-I curve.
Observe that in the open-circuit case, a barrier voltage develops, making n more positive than p, and limiting the diffusion current to a value exactly equal to the drift current , thus resulting in a zero current at the junction terminals, as should be the case since the terminals are open circuited.
Consider now the reverse-bias case in (b). The externally applied reverse-bias voltage is in the direction to add to the barrier voltage, and it does, thus increasing the effective barrier voltage to as shown. This reduces the number of holes that diffuse into the n region and the number of electrons that diffuse into the p. The end result is that the diffusion current is dramatically reduced.

## Slide 66
Figure to right shows pn-junction under three conditions:
  (a) open-circuit – where a barrier voltage V0 exists.
  (b) reverse bias – where a dc voltage VR is applied.
  (c) forward bias – where a dc voltage VF is applied.
Figure 3.11: The pn junction in: (a) equilibrium; (b) reverse bias; (c) forward bias.
1) no voltage applied
2) voltage differential across depletion zone is V0
3) ID = IS
1) negative voltage applied
2) voltage differential across depletion zone is V0 + VR
3) ID < IS
1) positive voltage applied
2) voltage differential across depletion zone is V0 - VF
3) ID > IS

## Slide 67: 5.1. Qualitative Description of Junction Operation

## Slide 68: 5.1. Qualitative Description of Junction Operation
reverse bias case
  the externally applied voltage VR adds to the barrier voltage V0
    …increase effective barrier
  this reduces rate of diffusion, reducing ID
    if VR > 1V, ID will fall to 0A
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct small drift current IS
forward bias case
  the externally applied voltage VF subtracts from the barrier voltage V0
    …decrease effective barrier
  this increases rate of diffusion, increasing ID
  the drift current IS is unaffected, but dependent on temperature
  result is that pn junction will conduct significant current ID - IS
minimal current flows in reverse-bias case
significant current flows in forward-bias case
Notes: So the diode is approximately a “one-way” valve!

## Slide 69: Forward-Bias Case
Observe that decreased barrier voltage will be accompanied by…
  (1) decrease in stored uncovered charge on both sides of junction
  (2) smaller depletion region
Width of depletion region shown to right.

## Slide 70: Reverse-Bias Case
Observe that increased barrier voltage will be accompanied by…
  (1) increase in stored uncovered charge on both sides of junction
  (2) wider depletion region
Width of depletion region shown to right.
Notes: Note that the diode in reverse bias looks like a parallel plate capacitor. Varactor diodes are used ac a voltage controlled capacitor.

## Slide 71: Reverse Biased Diode’s Application: Voltage-Dependent Capacitor
The PN junction can be viewed as a capacitor. By varying VR, the depletion width changes, changing its capacitance value; therefore, the PN junction is actually a voltage-dependent capacitor.

## Slide 72
Example 7: PN junctions

## Slide 74: 5.2. The Current-Voltage Relationship of the Junction
Q: What happens, exactly, when a forward-bias voltage (VF) is applied to the pn-junction?
  step #1: Initially, a small forward-bias voltage (VF) is applied. It, because of its polarity, pushes majority carriers (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
    Note, however, that this force is opposed by the built-in voltage (V0).

## Slide 75: step #1: Initially, a small forward-bias voltage (VF) is applied. It, because of its polarity, pushes majority (holes in p-region and electrons in n-region) toward the junction and reduces width of the depletion zone.
Figure: The pn junction with applied voltage.
VF
Note that, in this figure, the smaller circles represent minority carriers and not bound charges – which are not considered here.
P-type
N-type

## Slide 76: step #2: As the magnitude of VF increases, the depletion zone becomes thin enough such that the barrier voltage (V0 – VF) cannot stop diffusion current – as described in previous slides.
Figure: The pn junction with applied voltage.
VF
P-type
N-type

## Slide 77: step #3: Majority carriers (free electrons in n-region and holes in p-region) cross the junction and become minority charge carriers in the near-neutral region.
Figure: The pn junction with applied voltage.
diffusion current (ID)
drift current (IS)
VF
P-type
N-type

## Slide 78: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
Figure: The pn junction with applied voltage.
minority carrier concentration
location (x)
VF
For the open-circuit condition, minority carriers are evenly distributed throughout the non-depletion regions. This concentration is defined as either np0 or pn0.
pn0
np0
Figure: The pn junction with no applied voltage (open-circuited terminals).
P-type
N-type

## Slide 79: step #4: The concentration of minority charge carriers increases on either side of the junction. A steady-state gradient is reached as rate of majority carriers crossing the junction equals that of recombination.
VF
minority carrier concentration
location (x)
P-type
N-type

## Slide 80: step #5+: Diffusion current is maintained – in spite low diffusion lengths (e.g. microns) and recombination – by constant flow of both free electrons and holes towards the junction.
VF
flow of holes
flow of electrons
flow of diffusion current (ID)
recombination
Figure: The pn junction with applied voltage.
P-type
N-type

## Slide 81: PN junction Characteristics
Conduction band
Valence band
P type
N type

## Slide 82: 5.2. The Current-Voltage Relationship of the Junction
Q: For forward-biased case, how is diffusion current (ID) defined?

## Slide 83: 5.2. The Current-Voltage Relationship of the Junction
saturation current (IS) – is the maximum reverse current which will flow through pn-junction.
  It is proportional to cross-section of junction (A).
  Typical value is 10-18A.
Figure 13: The pn junction I–V characteristic.

## Slide 84: Example 6: pn-Junction
Consider a forward-biased pn junction conducting a current of I = 0.1mA with following parameters:
  NA = 1018/cm3, ND = 1016/cm3, A = 10-4cm2, ni = 1.5e10/cm3, Lp = 5um, Ln = 10um, Dp (n-region) = 10cm2/s, Dn (p-region) = 18cm2/s
Q(a): Calculate IS .
Q(b): Calculate the forward bias voltage (V).
Q(c): Component of current I due to hole injection and electron injection across the junction.

## Slide 85
(a)

## Slide 87: 5.3 Reverse Breakdown
Notes: Zener breakdown occurs when the electric field in the depletion layer increases to the point of breaking covalent bonds and generating electron-hole pairs. The electrons generated in this way will be swept by the electric field into the n side and the holes into the p side. Thus these electrons and holes constitute a reverse current across the junction. Once the zener effect starts, a large number of carriers can be generated, with a negligible increase in the
junction voltage. Thus the reverse current in the breakdown region will be large and its value must be determined by the external circuit, while the reverse voltage appearing between the diode terminals will remain close to the specified breakdown voltage VZ.

## Slide 88: Zener breakdown
The electric field in the depletion layer increases to cause breaking covalent bonds and generating electron-hole pairs.
The electrons generated in this way will be swept by the electric field into the n side and the holes into the p side. Thus these electrons and holes constitute a reverse current across the junction.
Once the zener effect starts (VR=5V), a large number of carriers can be generated, with a negligible increase in the junction voltage. Thus the reverse current in the breakdown region will be large and its value must be determined by the external circuit.
the reverse voltage appearing between the diode terminals will remain close to the specified breakdown voltage VZ.

## Slide 89: Avalanche breakdown
The minority carriers that cross the depletion region under the influence of the electric field gain sufficient kinetic energy to be able to break covalent bonds in atoms with which they collide.
The carriers liberated by this process may have sufficiently high energy to be able to cause other carriers to be liberated in another ionizing collision.
This process keeps repeating in the fashion of an avalanche, with the result that many carriers are created that are able to support any value of reverse current, as determined by the external circuit, with a negligible change in the voltage drop across the junction.

## Slide 90: 5.3 Reverse Breakdown
The maximum reverse-bias potential that can be applied before entering the breakdown region is called the peak inverse voltage (referred to simply as the PIV rating) or the peak reverse voltage (denoted the PRV rating).

## Slide 91: 6. Capacitive Effects in the pn Junction
Depletion or Junction Capacitance
When a pn junction is reverse biased
Diffusion Capacitance
When a pn junction is forward biased
Where
I is the forward-bias current.
is the mean transit time of the junction.

## Slide 92: 6. Capacitive Effects in the pn Junction
junction capacitance:
due to the dipole in the transition region (associated with the charge stored in the depletion region).
Also called transition region capacitance or depletion layer capacitance.
Dominates under reverse bias conditions.
Charge storage (Diffusion) capacitance:
associated with the minority carrier charge stored in the n and p materials as a result of the concentration profiles established by carrier injection.
Also referred to as diffusion capacitance.
Dominant when the junction is forward biased.

## Slide 93
Summary of Important Equations

## Slide 94
Summary of Important Equations

## Slide 95: Summary (1)
Today’s microelectronics technology is almost entirely based on the semiconductor silicon. If a circuit is to be fabricated as a monolithic integrated circuit (IC), it is made using a single silicon crystal, no matter how large the circuit is.
In a crystal of intrinsic or pure silicon, the atoms are held in position by covalent bonds. At very low temperatures, all the bonds are intact; No charge carriers are available to conduct current. As such, at these low temperatures, silicone acts as an insulator.

## Slide 96: Summary (2)
At room temperature, thermal energy causes some of the covalent bonds to break, thus generating free electrons and holes that become available to conduct electricity.
Current in semiconductors is carried by free electrons and holes. Their numbers are equal and relatively small in intrinsic silicon.
The conductivity of silicon may be increased drastically by introducing small amounts of appropriate impurity materials into the silicon crystal – via process called doping.

## Slide 97: Summary (3)
There are two kinds of doped semiconductor: n-type in which electrons are abundant, p-type in which holes are abundant.
There are two mechanisms for the transport of charge carriers in a semiconductor: drift and diffusion.
Carrier drift results when an electric field (E) is applied across a piece of silicon. The electric field accelerates the holes in the direction of E and electrons oppositely. These two currents sum to produce drift current in the direction of E.

## Slide 98: Summary (4)
Carrier diffusion occurs when the concentration of charge carriers is made higher in one part of a silicon crystal than others. To establish a steady-state diffusion current, a carrier concentration must be maintained in the silicon crystal.
A basic semiconductor structure is the pn-junction. It is fabricated in a silicon crystal by creating a p-region in proximity to an n-region. The pn-junction is a diode and plays a dominant role in the structure and operation of transistors.

## Slide 99: Summary (5)
When the terminals of the pn-junction are left open, no current flows externally. However, two equal and opposite currents (ID and IS) flow across the junction. Equilibrium is maintained by a built-in voltage (V0). Note, however, that the voltage across an open junction is 0V, since V0 is cancelled by potentials appearing at the metal-to-semiconductor connection interfaces.
The voltage V0 appears across the depletion region, which extends on both sides of the junction.

## Slide 100: Summary (6)
The drift current IS is carried by thermally generated minority electrons in the p-material that are swept across the depletion region into the n-side. The opposite occurs in the n-material. IS flows from n to p, in the reverse direction of the junction. Its value is a strong function of temperature, but independent of V0.
Forward biasing of the pn-junction, that is applying an external voltage that makes p more positive than n, reduces the barrier voltage to V0 - V and results in an exponential increase in ID (while IS remains unchanged).