Optimal Generation Scheduling of Cascaded Hydrothermal System Using Genetic Algorithm and Constriction Factor Based Particle Swarm Optimization Technique

M.M. Salama, M.M. Elgazar, S.M. Abdelmaksoud, H.A. Henry

Abstract— In this paper, a genetic algorithm (GA) and particle swarm optimization with constriction factor (CFPSO) are proposed for solving the short term multi chain hydrothermal scheduling problem with non smooth fuel cost objective functions. The performance of the proposed techniques is demonstrated on hydrothermal test system comprising of three thermal units and four hydro power plants. A wide range of thermal and hydraulic constraints such as power balance constraint, minimum and maximum limits of hydro and thermal units, water discharge rate limits, reservoir volume limits, initial and end reservoir storage volume constraint and water dynamic balance constraint are taken into consideration. The simulation results obtained from the constriction factor based particle swarm optimization are compared with the outcomes obtained from the genetic algorithm to reveal the validity and verify the feasibility of the proposed methods. The test results show that the particle swarm optimization technique is better solution than genetic algorithm in terms of solution quality and computational time.

Index Terms— Hydrothermal Generation Scheduling, Valve Point Loading Effect, Genetic Algorithm (GA), Particle Swarm Optimization (PSO), Constriction Factor (CF)

——————————   (   ——————————

1	Introduction

T

HE hydrothermal generation scheduling plays an important role in the operation and planning of a power system. Since the operating cost of thermal power plant is very high compared to the operating cost of hydro power plant, the integrated operation of the hydro and thermal plants in the same grid has become the more economical [1]. The main objective of the short term hydro thermal scheduling problem is to determine the optimal generation schedule of the thermal and hydro units to minimize the total production cost over the scheduling time horizon (typically one day or one week) subjected to a variety of thermal and hydraulic constraints. The hydrothermal generation scheduling is mainly concerned with both hydro unit scheduling and thermal unit dispatching. The hydrothermal generation scheduling problem is more difficult than the scheduling of thermal power systems. Since there is no fuel cost associated with the hydro power generation, the problem of minimizing the total production cost of hydrothermal scheduling problem is achieved by minimizing the fuel cost of thermal power plants under the constraints of water available for the hydro power generation in a given period of time [2]. In short term hydrothermal scheduling problem, the reservoir levels at the start and the end of the optimization period and the hydraulic inflows are assumed known. In addition, the generating unit limits and the load demand over the scheduling interval are known. Several mathematical optimization techniques have been used to solve short term hydrothermal scheduling problems [3]. In the past, hydrothermal scheduling problem is solved using classical mathematical optimization methods such as dynamic programming method [4-5], lagrangian relaxation method [6-7], mixed integer programming [8], interior point method [9], gradient search method and Newton raphson method [2]. In these conventional methods simplifying assumptions are made in order to make the optimization problem more tractable. Thus, most of conventional optimization techniques are unable to produce optimal or near optimal solution of this kind of problems.  The computational time of these methods increases with the increase of the dimensionality of the problem. The most common optimization techniques based upon artificial intelligence concepts such as evolutionary programming [10-11], simulated annealing [12-14], differential evolution [15], artificial neural network [16-18], genetic algorithm [19 -22] and particle swarm optimization [23-27] have been given attention by many researchers due to their ability to find an almost global or near global optimal solution for short term hydrothermal scheduling problems with operating constraints. Major problem associated with these techniques is that appropriate control parameters are required. Sometimes these techniques take large computational time due to improper selection of the control parameters.

The PSO is a population based optimization technique first proposed by Kennedy and Eberhart in 1995. In PSO, each particle is a candidate solution to the problem. Each particle in PSO makes its decision based on its own experience together with other particles experiences. Particles approach to the optimum solution through its present velocity, previous experience and the best experience of its neighbors [28]. Compared to other evolutionary computation techniques, PSO can solve the problems quickly with high quality solution and stable convergence characteristic, whereas it is easily implemented.

The genetic algorithm (GA) is a stochastic global search and optimization method that mimics the metaphor of natural biological evolution such as selection, crossover and mutation. GA is started with a set of candidate solutions called population (represented by chromosomes). At each generation, pairs of chromosomes of the current population are selected to mate with each other to produce the children for the next generation. The chromosomes which are selected to form the new offspring are selected according to their fitness. In general, the chromosomes with higher fitness values have higher probability to reproduce and survive to the next generation. While the chromosomes with lower fitness values tend to be discarded. This process is repeated until a termination condition is reached (for example maximum number of generations). Most of the GA parameters are set after considerable experimentation and the major drawback of this method is the lack of a solid theoretical basis for their setting.

# 2	problem formulation

The main objective of short term hydro thermal scheduling problem is to minimize the total fuel cost of thermal power plants over the optimization period while satisfying all thermal and hydraulic constraints. The objective function to be minimized can be represented as follows:

(1)

In general, the fuel cost function of thermal generating unit i at time interval t can be expressed as a quadratic function of real power generation as follows:

(2)                     Where  is the real output power of thermal generating unit i  at time interval t in (MW), Fit (Pgit) is the operating fuel cost of thermal unit i in ($/hr), FT is the total fuel cost of the system in ($), T is the total number of time intervals for the scheduling horizon, nt is the numbers of hours in scheduling time interval t, N is the total number of thermal generating units, and  ci  are the fuel cost coefficients of thermal generating unit i.

The generating units with multi-valve steam turbines exhibit a greater variation in the fuel cost function. The valve opening process of multi-valve steam turbines result in ripples in fuel cost curve [29]. Due to the valve point effects, the real input-output characteristic contains higher order non linearity and discontinuity which result in non smooth and non convex fuel cost functions. The valve point effects are taken into consideration by adding rectified sinusoidal cost function to the original fuel cost function described in (2). The fuel cost function of thermal power plant with valve point loading effect can be expressed as:

(3)

Where Fitv (Pgit) is the fuel cost function of thermal unit i including the valve point loading effect and fi, ei are the fuel cost coefficients of generating unit i with valve point loading effect.

The minimization of the objective function of short term hydrothermal scheduling problem is subject to a number of thermal and hydraulic constraints. These constraints include the following:

1) Real Power Balance Constraint:

For power balance, an equality constraint should be satisfied. The total active power generation from the hydro and thermal plants must equal to the total load demand plus transmission line losses at each time interval over the scheduling period.

(4)

Where, PDt is the total load demand during the time interval t in (MW), Phjt is the power generation of hydro unit j at time interval t in (MW), Pgit is the power generation of thermal generating unit i at time interval t in (MW) and PLt represents the total transmission line losses during the time interval t in (MW). For simplicity, the transmission power loss is neglected in this paper.

2) Thermal Generator Limit Constraint:

The output power generation of thermal power plant must lie in between its minimum and maximum limits. The inequality constraint for each thermal generator can be expressed as:

(5)

Where Pgimin and Pgimax are the minimum and maximum power outputs of thermal generating unit i in (MW), respectively. The maximum output power of thermal generator i is limited by thermal consideration and minimum power generation is limited by the flame instability of a boiler.

3) Hydro Generator Limit Constraint:

The output power generation hydro power plant must lie in between its minimum and maximum bounds. The inequality constraint for each hydro generator can be defined as:

(6)

Where Phjmin is the minimum power generation of hydro generating unit j in (MW) and Phjmax is the maximum power generation of hydro generating unit j in (MW).

4) Reservoir Storage Volume Constraint:

The operating volume of reservoir storage limit must lie in between the minimum and maximum capacity limits.

(7)

Where Vhjmin is the minimum storage volume of reservoir j and Vhjmax is the maximum storage volumes of reservoir j.

5) Water Discharge Rate Limit Constraint:

The water Discharge rate of hydro turbine must lie in between its minimum and maximum operating limits.

(8)

Where qhjmin and qhjmax are the minimum and maximum water discharge rate of reservoir j, respectively

6) Initial and End Reservoir Storage Volume Constraint:

This constraint implies that the desired volume of water to be discharged by each reservoir over the scheduling period should be in limit

(9)

(10)

Where Vhjbegin and Vhjend are the initial and final storage volumes of reservoir j, respectively

7) Water Dynamic Balance Constraint:

The water continuity equation relates the previous interval water storage in reservoirs with the current storage including delay in water transportation between successive reservoirs. The water continuity equation can be represented as:                            (11)

Where Ihjt is water inflow rate of reservoir j at time interval t, Shjt is the spillage from reservoir j at time interval t, τuj is the water transport delay from reservoir u to reservoir j and Ruj is the number of upstream hydro reservoirs directly above the reservoir j.

8) Hydro Plant Power Generation Characteristic:

The hydro power generation is a function of the net hydraulic head, water discharge rate and the reservoir volume. This can be expressed as follows:

and                                  (12)

The hydro power generation can be expressed in terms of reservoir volume instead of using the reservoir effective head, and the frequently used functional is:

(13)

Where c1j, c2j, c3j, c4j, c5j and c6j are the Power generation coefficients of hydro generating unit j

# 3	GENETIC ALGORITHM (GA)

The GA is a method for solving optimization problems that is based on natural selection, the process that drives biological evolution. The general scheme of GA is initialized with a population of candidate solutions (called chromosomes). Each chromosome is evaluated and given a value which corresponds to a fitness level in problem domain. At each generation, the GA selects chromosomes from the current population based on their fitness level to produce offspring. The chromosomes with higher fitness levels have higher probability to become parents for the next generation, while the chromosomes with lower fitness levels to be discarded. After the selection process, the crossover operator is applied to parent chromosomes to produce new offspring chromosomes that inherent information from both sides of parents by combining partial sets of genes from them. The chromosomes or children resulting from the crossover operator will now be subjected to the mutation operator in final step to form the new generation. Over successive generations, the population evolves toward an optimal solution. A schematic outline of simple genetic algorithm is illustrated in figure 1.

The features of GA are different from other traditional methods of optimization in the following respects [30]:

- GA does not require derivative information or other auxiliary knowledge.

- GA work with a coding of parameters instead of the parameters themselves. For simplicity, binary coded is used in this paper.

- GA search from a population of points in parallel, not a single point.

- GA use probabilistic transition rules, not deterministic rules.

## 3.1	Genetic Algorithm Operators

At each generation, GA uses three operators to create the new population from the previous population:

### Selection or Reproduction

Selection operator is usually the first operator applied on the population. The chromosomes are selected based on the Darwin's evolution theory of survival of the fittest. The chromosomes are selected from the population to produce offspring based on their fitness values. The chromosomes with higher fitness values are more likely to contributing offspring and are simply copied on into the next population. The commonly used reproduction operator is the proportionate reproduction operator. The ith string in the population is selected with a probability proportional to where, is the fitness value for that string. The probability of selecting the ith string is:

(14)

Where n is the population size, the commonly used selection operator is the roulette-wheel selection method. Since the circumference of the wheel is marked according to the string fitness, the roulette-wheel mechanism is expected to make  copies of the ith string in the mating pool. The average fitness of the population is:

(15)

### Crossover or Recombination

The basic operator for producing new chromosomes in the GA is that of crossover. The crossover produce new chromosomes have some parts of both parent chromosomes. The simplest form of crossover is that of single point crossover. In single point crossover, two chromosomes strings are selected randomly from the mating pool. Next, the crossover site is selected randomly along the string length and the binary digits are swapped between the two strings at crossover site.

### Mutation

The mutation is the last operator in GA. It prevents the premature stopping of the algorithm in a local solution. The mutation operator enhances the ability of the genetic algorithm to find a near optimal solution to a given problem by maintaining a sufficient level of genetic variety in the population. This operator randomly flips or alters one or more bits at randomly selected locations in a chromosome from 0 to 1 or vice versa.

### Parameters of Genetic Algorithm

The performance of GA depends on choice of GA parameters such as:

i. Population size (Np): The population size affects the efficiency and performance of the algorithm. Higher population size increases its diversity and reduces the chances of premature converge to a local optimum, but the time for the population to converge to the optimal regions in the search space will also increase. On the other hand, small population size may result in a poor performance from the algorithm. This is due to the process not covering the entire problem space. A good population size is about 20-30, however sometimes sizes 50-100 are reported as best.

ii. Crossover rate: The crossover rate is the parameter that affect the rate at which the process of cross over is applied. This rate generally should be high, about 80-95%.

iii. Mutation rate: It is a secondary search operator which increases the diversity of the population. Low mutation rate helps to prevent any bit position from getting trapped at a single value, whereas high mutation rate can result in essentially random search. This rate should be very low.

### Termination of Genetic Algorithm

The generational process is repeated until a termination condition has been satisfied. The common terminating conditions are: fixed number of generations reached, a best solution is not changed after a set number of iterations, or a cost that is lower than an acceptable minimum.

# 4	GA APPLIED TO SHORT TERM HYDRO- THERMAL SCHEDULING PROBLEM

In genetic algorithm, the water discharge through the turbines during each optimization interval is used as the main control variable. In binary genetic algorithm representation, the water discharge rates for each reservoir at each time interval are represented by a given number of binary strings. In GA binary representation, the water discharge rate is used rather than the output power generation of hydro units because the encoded parameter is more beneficial for dealing with water balance constraints. The binary representation of hydro thermal coordination problem is illustrated in figure 2.

Fig.2. Binary representation of hydrothermal scheduling problem

The generated string can be converted in the feasible range by using the following equation:

(16)

Where qhjmin is the minimum value of discharge rate through hydro turbine j, qhjmax is the maximum value of discharge rate through hydro turbine j, L is the String length (number of bits used for encoding water discharge rate of each hydro unit) and di is the binary coded value of the string ( decimal value of string).

By knowing the water discharge rate of each hydro power plant, the reservoir inflows and the hydro unit characteristic equation, the reservoir storage level and the output power of hydro power plant can be determined. The total power generations of all hydro power plants are subtracted from the total system load demand for each hour. The remaining load must be satisfied by running thermal units for each hour. An economic load dispatch problem is achieved and the fuel cost for each thermal unit over the scheduling period is calculated.

# 5	ALGORITHM FOR SHORT TERM HYDRO- THERMAL SCHEDULING USING GA METHOD

The sequential steps of solving short term hydro thermal scheduling problem by using genetic algorithm are explained as follows:

Step 1: Read the system input data, namely fuel cost curve coefficients, power generation limits of hydro and thermal units, number of thermal units, number of hydro units, power demands, power generation coefficients of hydro units, water volume limits, discharge rate limits and water inflow rate through the hydro turbines.

Step 2: Select genetic algorithm parameters such as population size, length of string, probability of crossover, probability of mutation and maximum number of generations to be performed.

Step 3: Generate the initial population randomly in the binary form. The initial population must be feasible candidate solutions that satisfy the practical operation constraints of all thermal and hydro units.

Step 4: Calculate the discharge rate of each hydro unit from the decoded population by using equation (16).

Step 5: Check the inequality constraint of the water discharge rate for each hydro unit from the following equation:

(17)

Step 6: Calculate the water storage volume of each reservoir from the water balance continuity equation defined in (11).

Step 7: Check the inequality constraint of reservoir storage volume for each hydro unit by the following equation:

(18)

Step 8: Calculate the hydro power generation of each hydro unit from the hydro power characteristic equation given in (13).

Step 9: Calculate the thermal demand by subtracting the generation of hydro units from the total load demand. The thermal demand (total load – hydro generation) must be covered by the thermal units. The thermal generations are calculated from the power balance equation given in (4).

Step 10: Calculate the output power of each thermal unit by solving economic load dispatch problem.

Step 11: Check the inequality constraint of thermal power generation for each thermal unit according to the following equation:

(19)

Step 12: Evaluate the fitness value for each string in the population by using the objective function stated in equation (1).

Step 13: The chromosomes with lower cost function are selected to become parents for the next generation.

Step 14: Perform the crossover operator to parent chromosomes to create new offspring chromosomes.

Step 15: The mutation operator is applied to the new offspring resulting from the crossover operation to form the new generation.

Step16: Update the population.

Step 17: If the number of iterations reached the maximum, then go to step19. Otherwise go to step 4.

Step18: The string that generates the minimum total fuel cost of the thermal power plants is the optimal solution of the problem.

Step 19: Print the outputs of hydrothermal scheduling and stop.

# 6	PARTICLE SWARM OPTIMIZATION WITH CONSTRICTION FACTOR

## 6.1	Overview of Particle Swarm Optimization (PSO)

Particle swarm optimization (PSO) is a population based stochastic optimization technique, inspired by social behavior of bird flocking or fish schooling. It is one of the most modern heuristic algorithms, which can be used to solve non linear and non continuous optimization problems. PSO shares many similarities with evolutionary computation techniques such as genetic algorithm (GA). The system is initialized with a population of random solutions and searches for optima by updating generations. However, unlike GA, PSO has no evolution operators such as mutation and crossover. The PSO algorithm searches in parallel using a group of random particles. Each particle in a swarm corresponds to a candidate solution to the problem. Particles in a swarm approach to the optimum solution through its present velocity, its previous experience and the experience of its neighbors. In every generation, each particle in a swarm is updated by two best values. The first one is the best solution (best fitness) it has achieved so far. This value is called Pbest. Another best value that is tracked by the particle swarm optimizer is the best value, obtained so far by any particle in the population. This best value is a global best and called gbest. Each particle moves its position in the search space and updates its velocity according to its own flying experience and neighbor's flying experience. After finding the two best values, the particle update its velocity according to equation (20).

(20)

Where Vik is the velocity of particle i at iteration k, Xik is the position of particle i at iteration k, ω is the inertia weight factor, c1and c2 are the acceleration coefficients, r1and r2 are positive random numbers between 0 and 1, Pbestik is the best position of particle i at iteration k and gbestk is the best position of the group at iteration k.

In the velocity updating process, the acceleration constants c1, c2 and the inertia weight factor are predefined and the random numbers r1and r2 are uniformly distributed in the range of [0,1]. Suitable selection of inertia weight in equation (20) provides a balance between local and global searches, thus requiring less iteration on average to find a sufficiently optimal solution. A low value of inertia weight implies a local search, while a high value leads to global search. As originally developed, the inertia weight factor often is decreased linearly from about 0.9 to 0.4 during a run. It was proposed in [31].  In general, the inertia weight ω is set according to the following equation:

(21)

Where ωmin and ωmax are the minimum and maximum value of inertia weight factor, Itermax corresponds to the maximum iteration number and Iter is the current iteration number.

The current position (searching point in the solution space) can be modified by using the following equation:

(22)

The velocity of particle i at iteration k must lie in the range:

(23)

The parameter Vmax determines the resolution or fitness, with which regions are to be searched between the present position and the target position. If is too high, the PSO facilitates a global search and particles may fly past good solutions. Conversely, if Vmax is too small, the PSO facilitates a local search and particles may not explore sufficiently beyond locally good solutions. In many experiences with PSO, Vmax was often set at 10-20% of the dynamic range on each dimension.

The constants c1 and c2 in equation (20) pull each particle towards Pbest and gbest positions. Thus, adjustment of these constants changes the amount of tension in the system. Low values allow particles to roam far from target regions, while high values result in abrupt movement toward target regions. Figure 3 shows the search mechanism of particle swarm optimization technique using the modified velocity, best position of particle i and best position of the group.

Fig.3. Updating the position mechanism of PSO technique

## Constriction Factor Approach

After the original particle swarm proposed by Kennedy and Eberhart, a lot of improved particle swarms were introduced. The particle swarm with constriction factor is very typical. Recent work done by Clerc [32] indicates that the use of a constriction factor may be necessary to insure convergence of the particle swarm optimization algorithm. In order to insure convergence of the particle swarm optimization algorithm, the velocity of the constriction factor approach can be represented as follows:

(24)

Where K is the constriction factor and given by:

(25)

Where:,

The convergence characteristic of the particle swarm optimization technique can be controlled byIn the constriction factor approach,must be greater than 4.0 to guarantee the stability of the PSO algorithm. However, asincreases the constriction factor decreases and diversification is reduced, yielding slower response. Typically, when the constriction factor is used, is set to 4.1 (i.e. c1 =c2 = 2.05) and the constant multiplier k is 0.729. The constriction factor approach can generate higher quality solutions than the basic PSO technique.

# 7	ALGORITHM FOR SHORT TERM HYDRO- THERMAL SCHEDULING USING CFPSO METHOD

The sequential steps of solving short term hydro thermal scheduling problem by using genetic algorithm are explained as follows:

Step 1: Read the system input data, namely fuel cost curve coefficients, power generation limits of hydro and thermal units, number of thermal units, number of hydro units, power demands, power generation coefficients of hydro power plants, upper and lower limits of reservoir volumes, discharge rate limits and water inflow rate through the hydro turbines.

Step 2: Initialize a population of particles with random positions according to the minimum and maximum operating limits of each unit (upper and lower bounds of power output of thermal generating units and upper and lower bounds of water discharge rate of hydro units). These initial particles must be feasible candidate solutions that satisfy the practical operation constraints of all thermal and hydro units.

Step 3: Initialize the velocity of particles in the range between.

Step 4: Calculate the reservoir storage of jth hydro power plant in the dependent interval by using the water balance continuity equation defined in (11).

Step5: Check the inequality constraint of reservoir storage volume according to equation (18).

Step 6: Calculate the hydro power generation from the equation given in (13).

Step 7: Calculate the thermal demand by subtracting the generation of hydro units from the total load demand. The thermal demand (total load – hydro generation) must be covered by the thermal units. The thermal generations are calculated from the power balance equation given in (4).

Step 8: Check the inequality constraint of thermal power generated using equation (19).

Step 9: Evaluate the fitness value of each particle in the population using the objective function given in equation (1).

Step 10: If the evaluation value of each particle is better than the previous Pbest, then set Pbest equal to the current value.

Step 11: Select the particle with the best fitness value of all the particles in the population as the gbest.

Step 12: Update the velocity of each particle according to equation (24).

Step 13: Check the velocity of each particle according to the following equation:

(26)

Step 14: The position of each particle is modified according to equation (15).

Step 15: Check the inequality constraints of the modified position.

Step 16: If the stopping criterion is reached (i.e. usually maximum number of iterations) go to step 17, otherwise go to step 4.

Step 17: The particle that generates the latest gbest is the optimal generation power of each unit with minimum total fuel cost of the thermal power plants.

Step 18: Print the outputs of hydrothermal scheduling and stop.

# 8	CASE STUDY AND SIMULATION RESULTS

To verify the feasibility and effectiveness of the proposed algorithms, a hydrothermal power system consists of a multi chain cascade of four hydro units and three thermal units were tested. The effect of valve point loading has been taken into account in this case study to illustrate the robustness of the proposed methods. The transport time delay between cascaded reservoirs is also considered in this case study. The scheduling time period is one day with 24 intervals of one hour each. The data of test system are taken from [17] and [18]. The multi chain hydro sub system configuration is shown in figure 2. The water time transport delays between connected reservoirs are given in table 1. In this case study, the output power of hydro power plants is represented as a function of the reservoir storage and the water discharge rates. The hydro power generation coefficients are given in table 2. The reservoir storage limits, discharge rate limits, initial and end reservoir storage volume conditions and the generation limits of hydro power plants are shown in table 3 while table 4 shows the reservoir inflows of multi chain hydro power plants. The fuel cost coefficients and the minimum and maximum limits of three thermal generating units are given in table 5. The load demand over the 2hours is given in table 6. The proposed algorithms has been implemented in MATLAB language and executed on an Intel Core i3, 2.27 GHz personal computer with a 3.0 GB of RAM. The optimal control parameters used in genetic algorithm are listed in table 7. The PSO control parameters selected for the solution are given in table 8. The program is run 50 times for each algorithm and the best among the 50 runs are taken as the final solutions. The resultant optimal schedule of thermal and hydro power plants and the hourly total fuel cost obtained from the genetic algorithm and the particle swarm optimization technique are shown in table 9 and table 10, respectively. Table 11 and table 12 shows the optimal hourly water discharge of hydro power plants obtained from the genetic algorithm and the particle swarm optimization techniques.  Table 13 shows the comparison of total fuel cost and computation time between the two proposed methods. From table 13, it is observed that the constriction factor based PSO algorithm give high quality solution with less computation time when compared to the genetic algorithm. Figure 5 to figure 8 shows the discharge trajectories of hydro power plants by using two proposed approaches, figure 9 to figure 11 gives the fuel cost of each thermal unit versus day hours by using the two proposed techniques and figure 12 presents the total fuel cost of the system versus 24 hours by using the two proposed methods.

Fig.3. Multi chain hydro sub system networks

Table 1: Water time transport delays between connected reservoirs

| Plant | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Ru | 0 | 0 | 2 | 1 |
|  | 2 | 3 | 4 | 0 |
| Ru : Number of upstream hydro power plants : Time delay to immediate downstream hydro power plants |

Table 2: Hydro power generation coefficients

| Plant | C1 | C2 | C3 | C4 | C5 | C6 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | -0.0042 | -0.4200 | 0.0300 | 0.9000 | 10.000 | -50.000 |
| 2 | -0.0040 | -0.3000 | 0.0150 | 1.1400 | 9.5000 | -70.000 |
| 3 | -0.0016 | -0.3000 | 0.0140 | 0.5500 | 5.5000 | -40.000 |
| 4 | -0.0030 | -0.3100 | 0.0270 | 1.4400 | 14.000 | -90.000 |

Table 3: Reservoir storage capacity limits, plant discharge limits, plant generation limits and reservoir end conditions

()

| Plant | Vhmin | Vhmax | Vhini | Vhend | qhmin | qhmax | Phmin | Phmax |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 80 | 150 | 100 | 120 | 5 | 15 | 0 | 500 |
| 2 | 60 | 120 | 80 | 70 | 6 | 15 | 0 | 500 |
| 3 | 100 | 240 | 170 | 170 | 10 | 30 | 0 | 500 |
| 4 | 70 | 160 | 120 | 140 | 13 | 25 | 0 | 500 |

Table 4: Reservoir inflows of multi chain hydro plants ()

| Hour | Reservoir | Hour | Reservoir |
| --- | --- | --- | --- |
|  | 1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 |
| 1 | 10 | 8 | 8.1 | 2.8 | 13 | 11 | 8 | 4 | 0 |
| 2 | 9 | 8 | 8.2 | 2.4 | 14 | 12 | 9 | 3 | 0 |
| 3 | 8 | 9 | 4 | 1.6 | 15 | 11 | 9 | 3 | 0 |
| 4 | 7 | 9 | 2 | 0 | 16 | 10 | 8 | 2 | 0 |
| 5 | 6 | 8 | 3 | 0 | 17 | 9 | 7 | 2 | 0 |
| 6 | 7 | 7 | 4 | 0 | 18 | 8 | 6 | 2 | 0 |
| 7 | 8 | 6 | 3 | 0 | 19 | 7 | 7 | 1 | 0 |
| 8 | 9 | 7 | 2 | 0 | 20 | 6 | 8 | 1 | 0 |
| 9 | 10 | 8 | 1 | 0 | 21 | 7 | 9 | 2 | 0 |
| 10 | 11 | 9 | 1 | 0 | 22 | 8 | 9 | 2 | 0 |
| 11 | 12 | 9 | 1 | 0 | 23 | 9 | 8 | 1 | 0 |
| 12 | 10 | 8 | 2 | 0 | 24 | 10 | 8 | 0 | 0 |

Table 5: Fuel cost coefficients and operating limits of thermal units

| Unit | ai | bi | ci | ei | fi | Pgi min | Pgi,max |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.0012 | 2.45 | 100 | 160 | 0.038 | 20 | 175 |
| 2 | 0.0010 | 2.32 | 120 | 180 | 0.037 | 40 | 300 |
| 3 | 0.0015 | 2.10 | 150 | 200 | 0.035 | 50 | 500 |

Table 6: Load demand for 24 hour

| Hour | PD (MW) | Hour | PD (MW) | Hour | PD (MW) | Hour | PD (MW) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 750 | 7 | 950 | 13 | 1110 | 19 | 1070 |
| 2 | 780 | 8 | 1010 | 14 | 1030 | 20 | 1050 |
| 3 | 700 | 9 | 1090 | 15 | 1010 | 21 | 910 |
| 4 | 650 | 10 | 1080 | 16 | 1060 | 22 | 860 |
| 5 | 670 | 11 | 1100 | 17 | 1050 | 23 | 850 |
| 6 | 800 | 12 | 1150 | 18 | 1120 | 24 | 800 |

Table 7: Control parameters of genetic algorithm

| Genetic algorithm parameters | Value |
| --- | --- |
| Population size | 50 |
| Maximum number of generations | 300 |
| Crossover probability | 0.8 |
| Mutation probability | 0.05 |

Table 8: Control parameters of particle swarm optimization

| Genetic algorithm parameters | Value |
| --- | --- |
| Population size | 50 |
| Maximum number of generations | 300 |
| Acceleration coefficients(c1/c2) | 2.05 |
| Minimum inertia weight (ωmin) | 0.4 |
| Minimum inertia weight (ωmax) | 0.9 |
| Constriction factor (k) | 0.729 |

Table 9: Hourly optimal hydrothermal generation schedule using genetic algorithm

| Hour | Thermal generation (MW) | Hydro generation (MW) | Total fuel cost ($/hr) |
| --- | --- | --- | --- |
|  | Pg1 | P2g | Pg3 | Ph1 | Ph2 | Ph3 | Ph4 |  |
| 1 | 23.1236 | 295.3239 | 50.0000 | 64.5640 | 81.4962 | 24.6730 | 210.8193 | 1331.356 |
| 2 | 102.7101 | 133.1556 | 140.0197 | 90.4459 | 71.3577 | 42.8051 | 199.5059 | 1340.523 |
| 3 | 20.0000 | 125.0555 | 231.9288 | 70.2375 | 53.9426 | 27.6694 | 171.1662 | 1310.812 |
| 4 | 21.4101 | 45.0040 | 229.4431 | 82.1908 | 67.5285 | 47.5866 | 156.8370 | 1132.477 |
| 5 | 105.9331 | 129.7690 | 145.1922 | 54.6509 | 46.2334 | 24.2977 | 163.9238 | 1387.198 |
| 6 | 26.0101 | 293.1966 | 142.0860 | 53.1216 | 55.7626 | 47.1213 | 182.7018 | 1592.036 |
| 7 | 30.3361 | 296.2658 | 234.1831 | 65.6663 | 75.4587 | 50.2856 | 197.8044 | 1898.590 |
| 8 | 105.3821 | 300.0000 | 229.9113 | 74.1777 | 60.1855 | 53.8578 | 186.4857 | 2043.714 |
| 9 | 163.2261 | 286.1469 | 319.0854 | 60.4050 | 43.9982 | 29.5776 | 187.5608 | 2547.151 |
| 10 | 116.2331 | 294.1784 | 317.9356 | 68.8611 | 49.2068 | 43.3024 | 190.2826 | 2351.185 |
| 11 | 102.4704 | 210.1291 | 415.0816 | 79.7521 | 45.5969 | 53.2064 | 193.7635 | 2340.721 |
| 12 | 112.0361 | 126.2291 | 498.8067 | 104.4852 | 58.7410 | 54.3342 | 195.3676 | 2453.624 |
| 13 | 22.1319 | 294.9565 | 402.5905 | 95.3191 | 43.6388 | 47.9560 | 203.4072 | 2343.924 |
| 14 | 104.2409 | 207.1327 | 320.9477 | 91.9101 | 56.9260 | 40.8118 | 208.0307 | 2029.419 |
| 15 | 149.0448 | 298.0445 | 141.1267 | 100.2612 | 60.8535 | 51.1703 | 209.4990 | 2057.058 |
| 16 | 130.1147 | 123.3982 | 409.0408 | 87.6299 | 51.4138 | 43.7312 | 214.6714 | 2268.834 |
| 17 | 102.9447 | 295.1445 | 233.2934 | 93.7531 | 44.0839 | 57.7723 | 223.0082 | 2009.123 |
| 18 | 172.0170 | 209.7859 | 315.2614 | 89.2480 | 51.2182 | 54.4402 | 228.0293 | 2274.654 |
| 19 | 103.0447 | 295.2660 | 276.1546 | 65.2651 | 43.1068 | 60.3307 | 226.8321 | 2307.208 |
| 20 | 22.2443 | 295.1658 | 319.2717 | 68.2697 | 49.0082 | 57.8633 | 238.1771 | 2036.999 |
| 21 | 57.4388 | 209.1484 | 227.4860 | 69.2510 | 46.2793 | 50.7053 | 249.6913 | 1775.913 |
| 22 | 21.0737 | 213.1772 | 236.1372 | 62.6533 | 50.6642 | 41.7298 | 234.5646 | 1616.474 |
| 23 | 20.0000 | 294.7055 | 139.2702 | 58.7600 | 43.6722 | 53.3260 | 240.2661 | 1515.158 |
| 24 | 20.0000 | 140.1303 | 230.1860 | 69.8166 | 44.9844 | 55.9327 | 238.9501 | 1427.858 |

Table 10: Hourly optimal hydrothermal generation schedule using constriction factor based particle swarm optimization

| Hour | Thermal generation (MW) | Hydro generation (MW) | Total fuel cost ($/hr) |
| --- | --- | --- | --- |
|  | Pg1 | P2g | Pg3 | Ph1 | Ph2 | Ph3 | Ph4 |  |
| 1 | 102.3522 | 209.8194 | 57.6422 | 60.1722 | 80.3207 | 38.6494 | 201.0440 | 1345.009 |
| 2 | 20.0000 | 126.8176 | 230.7566 | 73.0700 | 79.3509 | 55.3298 | 194.6751 | 1315.606 |
| 3 | 105.4454 | 130.2316 | 139.7551 | 54.0153 | 55.8002 | 42.4402 | 172.3121 | 1335.646 |
| 4 | 25.1898 | 128.3247 | 141.6169 | 86.1289 | 65.3077 | 48.1490 | 155.2830 | 1141.171 |
| 5 | 123.6643 | 116.0352 | 140.8527 | 54.2512 | 43.3706 | 23.7179 | 168.1081 | 1479.744 |
| 6 | 20.2832 | 300.0000 | 144.4642 | 54.0606 | 73.2636 | 41.5883 | 166.3402 | 1610.288 |
| 7 | 32.7205 | 300.0000 | 230.9010 | 88.9708 | 71.1724 | 55.5877 | 170.6477 | 1921.262 |
| 8 | 101.6320 | 296.3523 | 234.4262 | 77.8782 | 70.3955 | 54.2548 | 175.0610 | 2032.832 |
| 9 | 104.6402 | 295.1020 | 365.9320 | 56.0490 | 37.4051 | 44.0579 | 186.8139 | 2594.627 |
| 10 | 110.1216 | 300.0000 | 319.4361 | 64.1774 | 44.9308 | 40.0597 | 201.2744 | 2344.922 |
| 11 | 102.9433 | 299.8210 | 324.6830 | 96.2948 | 46.6031 | 38.5205 | 191.1343 | 2333.356 |
| 12 | 29.9546 | 300.0000 | 410.6102 | 102.7084 | 56.2583 | 57.3524 | 193.1162 | 2450.648 |
| 13 | 20.0000 | 294.0590 | 408.0650 | 87.5439 | 45.7874 | 54.3512 | 200.1934 | 2306.124 |
| 14 | 20.1798 | 294.8191 | 319.1150 | 81.9074 | 51.3624 | 52.8587 | 209.7574 | 2016.600 |
| 15 | 65.0533 | 297.0703 | 229.3150 | 94.6490 | 50.6550 | 49.3154 | 223.9421 | 2047.800 |
| 16 | 116.1536 | 139.0801 | 406.3149 | 84.1369 | 53.9792 | 42.2257 | 218.1095 | 2301.257 |
| 17 | 103.0538 | 209.8115 | 317.8150 | 99.4313 | 47.9614 | 52.1143 | 219.8126 | 1997.518 |
| 18 | 35.3345 | 298.2462 | 320.2436 | 102.2590 | 69.0529 | 60.3747 | 234.4891 | 2183.483 |
| 19 | 102.0183 | 211.1061 | 321.2727 | 84.0163 | 40.2404 | 52.7194 | 258.6312 | 2022.778 |
| 20 | 100.0383 | 212.6210 | 313.3650 | 58.2941 | 42.5457 | 50.6354 | 272.5005 | 2046.704 |
| 21 | 29.9704 | 295.1772 | 140.3611 | 79.0149 | 64.9985 | 37.0795 | 263.3983 | 1607.165 |
| 22 | 109.9750 | 134.5710 | 232.0451 | 57.9149 | 42.6570 | 42.0930 | 240.7441 | 1676.804 |
| 23 | 103.0293 | 125.5876 | 230.0580 | 65.3415 | 42.4109 | 45.5238 | 238.0490 | 1515.265 |
| 24 | 22.6076 | 209.6222 | 140.0572 | 67.0476 | 49.5320 | 42.4138 | 268.7197 | 1299.011 |

Table 11: Hourly hydro plant discharge using ga

| Hour | ) )Hydro plant discharges |
| --- | --- |
|  | qh1 | qh2 | qh3 | qh4 |
| 1 | 6.3621 | 13.5605 | 22.9822 | 14.4752 |
| 2 | 10.8961 | 11.1072 | 18.4672 | 15.0222 |
| 3 | 7.1611 | 7.4198 | 20.5141 | 13.2766 |
| 4 | 9.2025 | 10.1168 | 15.4519 | 13.8298 |
| 5 | 5.2188 | 6.1660 | 21.8955 | 13.0000 |
| 6 | 5.0000 | 7.7210 | 16.4755 | 14.8439 |
| 7 | 6.4752 | 14.4394 | 15.9646 | 16.2453 |
| 8 | 7.6061 | 10.2842 | 12.7943 | 14.4014 |
| 9 | 5.7007 | 7.0449 | 21.0536 | 13.1672 |
| 10 | 6.6596 | 7.7579 | 18.1771 | 13.0000 |
| 11 | 8.0732 | 6.9097 | 14.3529 | 13.0000 |
| 12 | 14.6622 | 9.4728 | 13.3191 | 13.2459 |
| 13 | 11.1318 | 6.6146 | 17.4210 | 13.1229 |
| 14 | 10.2663 | 8.8766 | 19.3652 | 13.0000 |
| 15 | 12.5358 | 9.8090 | 17.1765 | 13.0000 |
| 16 | 9.4818 | 7.9669 | 19.4765 | 13.6146 |
| 17 | 10.8308 | 6.7253 | 14.2780 | 14.1678 |
| 18 | 9.9715 | 8.1882 | 17.3398 | 14.0903 |
| 19 | 6.2662 | 6.7990 | 13.7548 | 13.5286 |
| 20 | 6.6596 | 7.7364 | 16.4566 | 14.1924 |
| 21 | 6.7825 | 7.0449 | 19.2107 | 15.7536 |
| 22 | 5.9220 | 7.5981 | 21.0261 | 13.5409 |
| 23 | 5.4303 | 6.3073 | 17.7181 | 14.2170 |
| 24 | 6.7038 | 6.3335 | 16.3337 | 13.7808 |

Table 12: Hourly hydro plant discharge using cfpso method

| Hour | ) )Hydro plant discharges |
| --- | --- |
|  | qh1 | qh2 | qh3 | qh4 |
| 1 | 5.7990 | 12.9505 | 20.5398 | 13.1229 |
| 2 | 7.4559 | 14.9805 | 12.8725 | 13.9983 |
| 3 | 5.0000 | 8.2127 | 17.9687 | 13.0000 |
| 4 | 9.6117 | 10.3248 | 16.4797 | 13.0000 |
| 5 | 5.0528 | 6.1585 | 22.5614 | 13.4225 |
| 6 | 5.0000 | 14.3987 | 18.7684 | 13.2641 |
| 7 | 10.1422 | 14.1917 | 11.5845 | 13.0000 |
| 8 | 8.1422 | 13.8035 | 15.0767 | 13.0000 |
| 9 | 5.1849 | 6.0528 | 19.1534 | 13.0000 |
| 10 | 6.0564 | 6.9771 | 20.4840 | 14.0564 |
| 11 | 11.1414 | 7.0141 | 20.9517 | 13.0528 |
| 12 | 13.5567 | 8.7984 | 13.7150 | 13.0000 |
| 13 | 9.4322 | 6.8451 | 16.3067 | 13.0000 |
| 14 | 8.3885 | 7.5845 | 17.3808 | 13.1585 |
| 15 | 10.6153 | 7.2676 | 19.0765 | 13.8979 |
| 16 | 8.6736 | 7.7958 | 20.6765 | 13.1849 |
| 17 | 11.8519 | 6.7976 | 18.0101 | 13.0000 |
| 18 | 13.4021 | 12.1095 | 13.0102 | 14.2676 |
| 19 | 8.9637 | 6.1907 | 18.3101 | 17.0670 |
| 20 | 5.4306 | 6.3603 | 19.0075 | 18.9034 |
| 21 | 8.1710 | 10.8396 | 22.3957 | 17.3716 |
| 22 | 5.3689 | 6.2854 | 21.1805 | 14.6610 |
| 23 | 6.1983 | 6.0528 | 19.9457 | 13.8475 |
| 24 | 6.3625 | 7.0287 | 20.5701 | 17.4578 |

Table 13: comparison of total fuel cost and computation time between GA and CFPSO techniques

| Method | Total fuel cost ($) | CPU Time (Sec) |
| --- | --- | --- |
| CFPSO | 44925.62 | 183.64 |
| GA | 45392.009 | 198.57 |

Fig.5. Discharge trajectories of hydro plant 1 using GA and CFPSO

# 9	CONCLUSIONS

In this paper, the constriction factor based particle swarm optimization (CFPSO) technique and genetic algorithm (GA) are proposed for solving short term multi chain hydrothermal scheduling problem. To demonstrate the performance efficiency of the proposed algorithms, they has been applied on test system consists of a multi chain cascade of four hydro units and three thermal units. The effect of valve point loading is considered in this paper to demonstrate the robustness of the proposed techniques. The results obtained from the CFPSO technique are compared with the simulation results obtained from the GA to verify the feasibility of the proposed methods. The numerical results show that the CFPSO approach give a cheaper total generated cost than genetic algorithm. From the tabulated results, it is clear that the computational time of the CFPSO technique is less than the genetic algorithm. . Thus, the proposed CFPSO approach can converge to the minimum fuel cost faster than the GA method.

References

- A.J. Wood and B.F. Wollenberg, "Power Generation, Operation, and Control", John Wiley and Sons., New York, 1984.

- D.P. Kothari and J.S. Dhillon, "Power system optimization", New Delhi, India, Pvt. Ltd, 2009.

- I.A. Farhat and M.E. El-Hawary, "Optimization methods applied for solving the short term hydro thermal coordination problem", Electric Power System Research, vol. 79, pp. 1308-1320, 2009

- J. Tang and P.B. Luh, "Hydro thermal scheduling via extended differential dynamic programming and mixed coordination", IEEE Trans. Power Syst., vol. 10, no. 4 pp. 2021-2028, Nov.,1995.

- Y. Jin-Shyr and C. Nanming, "Short term hydro thermal coordination using multi pass dynamic programming", IEEE Trans. Power Syst., vol. 4, pp. 1050-1056, 1989.

- X. Guan, E. Ni, R. Li and P.B. Luh, " An optimization based algorithm for scheduling hydro thermal power systems with cascaded reservoirs and discrete hydro constraints", IEEE Trans. Power Syst., vol. 12, pp. 1775-1780, 1997.

- S. Al-Agtash, "Hydro thermal scheduling by augmented lagrangian: consideration of transmission constraints and pumped storage units", Power Engineering Review, IEEE, vol. 21, pp. 58-59, 2001.

- O. Nilsson and D. Sjelvgren, "Mixed integer programming applied to short term planning of  a hydro thermal system", IEEE Trans. Power Syst., vol. 11, pp. 281-286, 1996.

- L.M. Kimball, K.A. Clements, P.W. Davis and I. Nejdawi, "Multi period hydro thermal economic dispatch by an interior point method", Mathematical Problems in Engineering, vol. 8, pp. 33-42, 2002.

- J. Maturana, M-C. Riff," Solving the short-term electrical generation scheduling problem by an adaptive evolutionary approach", European Journal of Operational Research, vol. 179, pp. 677-691, 2007.

- N.C. Nayak and C.C.A. Rajan, "Hydro thermal scheduling by an evolutionary programming method with cooling-banking constraints", International Journal of Soft Computing and Engineering (IJSCE), Issue .3, vol. 2, pp. 517-521, July, 2012.

- D.P. Wong and Y.W. Wong, "Short term hydro thermal scheduling part. I. Simulated annealing approach", Generation, Transmission and Distribution, IEE Proceeding, vol. 141, pp. 497-501, 1994.

- D.P. Wong and Y.W. Wong, "Short term hydro thermal scheduling part. II. Parallel simulated annealing approach", Generation, Transmission and Distribution, IEE Proceeding, vol. 141, pp. 502-506, 1994.

- D.N. Simopoulos, S.D. Kavatza and C.D. Vournas, "An enhanced peak shaving method for short term hydro thermal scheduling", Energy Conversion and Management, vol. 48, pp. 3018-3024, 2007.

- T. Jayabarathi, S. Chalasani and Z.A. Shaik, "Hybrid differential evolution and particle swarm optimization based solutions to short term hydro thermal scheduling", WSEAS Trans. Power Syst., Issue 11, vol. 2, Nov.,2007.

- V.N. Diew and W. Ongsakul, "Enhanced merit order and augmented lagrange Hopfield network for hydro thermal scheduling", International Journal of Electrical Power & Energy Systems, vol. 30, no. 2, pp. 93-101, 2008.

- M. Basu, "Hopfield neural networks for optimal scheduling of fixed head hydro- thermal power systems", Electric Power Systems Research, vol. 64, no. 1, pp. 11-15, 2003.

- M. Basu, "An interactive fuzzy satisfying method based on evolutionary programming technique for multi objective short-term hydro thermal scheduling", Electric Power Systems Research, vol. 69, pp. 277-285, 2004.

- E. Gil, J. Bustos, H. Rudnick," Short term hydrothermal generation scheduling model using genetic algorithm", IEEE Trans. Power Syst. Vol. 18, no. 4, pp. 1256-1264, Nov., 2003.

- C.E. Zoumas, A.G. Bakirtzis, J.B. Theocharis, V. Petridis," A genetic algorithm solution approach to the hydro thermal coordination problem", IEEE Trans. Power Syst., vol. 19, no. 2, pp. 1356-1364, May, 2004.

- A. George, M.C. Reddy and A.Y. Sivaramakrishnan, "Short term hydro thermal scheduling based on multi-objective genetic algorithm", International Journal of Electrical Engineering, vol. 3, no. 1, pp. 13-26, 2010.

- S.O. Orero, M.R. Irving," A genetic algorithm modeling framework and solution technique for short term optimal hydrothermal scheduling", IEEE Trans. Power Syst., vol. 13, no. 2, pp. 501-518,May1998.

- S. Titus, A.E. Jeyakumar," Hydrothermal scheduling using an improved particle swarm optimization technique considering prohibited operating zones", International Journal of Soft Computing, vol. 2, no. 2, pp. 313-319, 2007.

- G. Sreenivasan, C.H. Saibabu, S. Sivanagaraju," PSO based short-term hydrothermal scheduling with prohibited discharge zones", International Journal of Advanced Computer Science and Applications, vol. 2, no. 9, pp. 97-105, 2011.

- C. Sun and S. Lu, "Short term combined economic emission hydro thermal scheduling using improved quantum-behaved particle swarm optimization", Expert Syst. App., vol. 37, pp. 4232-4241, 2010.

- K.K. Mandal and N. Chakraborty, "Optimal scheduling of cascaded hydro thermal systems using a new improved particle swarm optimization Technique", Smart Grid and Renewable Energy, vol.2, pp. 282-292, Aug., 2011.

- K.K. Mandal, M. Basu and N. Chakraborty, "Particle swarm optimization technique based short-term hydrothermal scheduling", Applied Soft Computing, pp. 1392-1399,2008.

- S.Y. Lim, M. Montakhab and H. Nouri, "Economic dispatch of power system using particle swarm optimization with constriction factor", International Journal of Innovations in Energy Syst. and Power, vol. 4, no. 2, pp. 29-34 Oct, 2009.

- J.B. Park, Y.W. Jeong, H.H. Kim and J.R. Shin," An improved particle swarm optimization for economic dispatch with valve-point effect", International Journal of Innovations in Energy Syst. And power, vol. 1, no. 1, pp. 1-7, Nov.2006.

- Y. Mimoun, M. Rahli and K. L. Abdelhakem," Economic power dispatch using Evolutionary Algorithm", Journal of Electrical Engineering, vol. 57, no. 4, PP. 211-217, 2006.

- Y. Shi and R.C. Eberhart, "Parameters selection in particle swarm optimization", Proceedings, of the Seventh Annual Conference on Evolutionary Programming, IEEE Press (1998).

- M. Clerc and J. Kennedy, "The particle swarm-explosion, stability, and convergence in a multidimensional complex space", IEEE Trans. on Evolutionary Computation, vol. 6, no. 1, pp. 58-73, Feb. 2002.

# Text boxes

Fig.1. Schematic outline of simple genetic algorithm

Fig.6. Discharge trajectories of hydro plant 2 using GA and CFPSO

Fig.7. Discharge trajectories of hydro plant 3 using GA and CFPSO

Fig.8. Discharge trajectories of hydro plant 4 using GA and CFPSO

Fig.9. Fuel cost of thermal unit 1 using GA and CFPSO

Fig.10. Fuel cost of thermal unit 2 using GA and CFPSO

Fig.11. Fuel cost of thermal unit 3 using GA and CFPSO

Fig.12. Total fuel cost of thermal units using GA and CFPSO