## Slide 1: Automatic Control
By
Dr. / Mohamed Ahmed Ebrahim Mohamed
E-mail: mohamedahmed_en@yahoo.com
Web site: http://bu.edu.eg/staff/mohamedmohamed033

## Slide 2
Lecture (1)

## Slide 3
BODE PLOT

## Slide 4
BODE PLOT
1
Introduction.
2
Frequency Response Definition.
Bode Plot Construction.
7
5
6
4
3
Bode Plot Definition.
Frequency Response Plot.
Viewpoints of analyzing control system behavior.
Logarithmic coordinate.

## Slide 5
Frequency Response Definition
What is frequency response of a system?
The frequency response of a system is defined as the steady-state response of the system to a sinusoidal input signal.
The sinusoid is a unique input signal, and the resulting output signal for a linear system, as well as signals throughout the system, is sinusoidal in the steady-state.

## Slide 6
Bode Plot Definition
What is Bode Plot?
Bode Plot is a (semi log) plot of the transfer function magnitude and phase angle as a function of frequency.

## Slide 7
Polar Plots
Frequency Response Plots

## Slide 8
The transfer function can be separated into magnitude and phase angle information
H(j) = |H(j)| Φ(j)
e.g.,
H(j)=Z(jw)
Frequency Response

## Slide 9
Routh-Hurwitz
Root locus
Bode diagram (plots)
Nyquist plots
Nicols plots
Time domain
Viewpoints of analyzing control system behavior

## Slide 10
L.T.I system
Magnitude:
Phase:
G(s)
H(s)
＋
－
Magnitude:
Phase:
Steady state response

## Slide 11
Decade :
Octave :
dB
Logarithmic coordinate
The gain magnitude is many times expressed in terms of decibels (dB)
dB = 20 log10 A
where A is the amplitude or gain
  a decade is defined as any 10-to-1 frequency range
  an octave is any 2-to-1 frequency range
  20 dB/decade = 6 dB/octave

## Slide 12
Case I : k
Magnitude:
Phase:
Bode Plot Construction

## Slide 13
Case II :
Magnitude:
Phase:

## Slide 14
Case III :
Magnitude:
Phase:

## Slide 15
Case IV :
Magnitude:
Phase:

## Slide 16
Case V :
Magnitude:
Phase:

## Slide 18
Case VI :

## Slide 20
Example :

## Slide 22
Minimum phase system
Type 0 : (i.e. n=0)
0dB/dec

## Slide 23
Type I : (i.e. n=1)
-20dB/dec
-40dB/dec

## Slide 24
Type 2 : (i.e. n=2)
-40dB/dec
-60dB/dec

## Slide 25
A transfer function is called minimum phase when all the poles and zeroes are LHP and non-minimum-phase when there are RHP poles or zeroes.
Minimum phase system
Stable
The gain margin (GM) is the distance on the bode magnitude plot from the amplitude at the phase crossover frequency up to the 0 dB point. GM=-(dB of GH measured at the phase crossover frequency)
The phase margin (PM) is the distance from -180 up to the phase at the gain crossover frequency. PM=180+phase of GH measured at the gain crossover frequency
Relative Stability

## Slide 26
Open loop transfer function :
Closed-loop transfer function :
Open loop Stability  poles of in LHP
Re
Im
RHP
Closed-loop Stability 
poles of in left side of (-1,0)

## Slide 27
Gain crossover frequency:
phase crossover frequency:
P.M.>0
G.M.>0
Stable system

## Slide 28
P.M.<0
G.M.<0
Stable system
Unstable system
Unstable system

## Slide 30
Straight-line approximations of the Bode plot may be drawn quickly from knowing the poles and zeroes
  response approaches a minimum near the zeroes
  response approaches a maximum near the poles
The overall effect of constant, zero and pole terms
Bode Plot Summary

## Slide 31
Express the transfer function in standard form
There are four different factors:
  Constant gain term, K
  Poles or zeroes at the origin, (j)±N
  Poles or zeroes of the form (1+ j)
  Quadratic poles or zeroes of the form 1+2(j)+(j)2
Bode Plot Summary

## Slide 32
We can combine the constant gain term (K) and the N pole(s) or zero(s) at the origin such that the magnitude crosses 0 dB at
Define the break frequency to be at ω=1/ with magnitude at ±3 dB and phase at ±45°
Bode Plot Summary

## Slide 33
where N is the number of roots of value τ
Bode Plot Summary

## Slide 34: Single Pole & Zero Bode Plots
ω
Pole at ωp=1/
Gain
Phase
ω
0°
–45°
–90°
One Decade
0 dB
–20 dB
ω
Zero at ωz=1/
Gain
Phase
ω
+90°
+45°
0°
One Decade
+20 dB
0 dB
ωp
ωz
Assume K=1
20 log10(K) = 0 dB

## Slide 35
Further refinement of the magnitude characteristic for first order poles and zeros is possible since
  Magnitude at half break frequency: |H(½b)| = ±1 dB
  Magnitude at break frequency: |H(b)| = ±3 dB
  Magnitude at twice break frequency: |H(2b)| = ±7 dB
Second order poles (and zeros) require that the damping ratio ( value) be taken into account; see Fig. 9-30 in textbook
Bode Plot Refinements

## Slide 36
We can also take the Bode plot and extract the transfer function from it (although in reality there will be error associated with our extracting information from the graph)
First, determine the constant gain factor, K
Next, move from lowest to highest frequency noting the appearance and order of the poles and zeros
Bode Plots to Transfer Function

## Slide 37
Frequency Response Plots
Bode Plots – Real Poles (Graphical Construction)

## Slide 38
Frequency Response Plots
Bode Plots – Real Poles

## Slide 39
Frequency Response Plots
Bode Plots – Real Poles

## Slide 40
Gain and Phase Margin
Let's say that we have the following system:
where K is a variable (constant) gain and G(s) is the plant under consideration.
The gain margin is defined as the change in open loop gain required to make the system unstable. Systems with greater gain margins can withstand greater changes in system parameters before becoming unstable in closed loop. Keep in mind that unity gain in magnitude is equal to a gain of zero in dB
The phase margin is defined as the change in open loop phase shift required to make a closed loop system unstable.
The phase margin is the difference in phase between the phase curve and -180 deg at the point corresponding to the frequency that gives us a gain of 0dB (the gain cross over frequency, Wgc).
Likewise, the gain margin is the difference between the magnitude curve and 0dB at the point corresponding to the frequency that gives us a phase of -180 deg (the phase cross over frequency, Wpc).

## Slide 41
Gain and Phase Margin
-180

## Slide 42
Examples - Bode

## Slide 43
Examples - Bode

## Slide 44
Examples – Bode

## Slide 45
Thank You
For Your Attention
Mohamed Ahmed Ebrahim