## Slide 1: Introduction To Compressible Flow

## Slide 2: Aims
Provide an introductory courses in Compressible flow

## Slide 3
Understand the definition and fundamental aspects of compressible flow
Understand the definitions and types of shock and expansion waves: oblique shock waves, shock expansion interaction, and unsteady expansion waves
Be able to do simple calculations related to applications of compressible flow on variations in geometry
Understand the concept of generalization of subsonic and supersonic flows

## Slide 4: • Introduction to compressible flows – Definitions and equations of compressible flow, Conservation laws, Sonic velocity and Mach number • Isentropic Flow (IF) – Equations of isentropic flows and stagnation properties, IF in a converging and converging-diverging nozzle, and application • Normal shock waves – Stationary and moving normal shock wave, Working equations and shocks in nozzles, and application • Adiabatic flow – Working equations, nozzle operation, and analysis of Fanno flow • Flow with heat transfer -Analysis of Rayleigh subsonic & supersonic flow. • Oblique shock wave – Working equations, Oblique shock analysis • Prandt-Meyer Flow – Analysis of Prandtl-Meyer flow – Shock-expansion interaction
Course Contents

## Slide 5
1- Fundamentals of Gas Dynamics by Robert D. Zucker : ISBN 0-916460-12-6
2- Gas Dynamics by James John and Theo Keith : ISBN 0-13-202331-8
3- Fundamental of Aerodynamics by John D. Anderson, Jr : ISBN 0-07- 001656-9
4- ANY lecture notes – Gas dynamics
5- Compressible fluid flow , Michal A. Saad
Recommended Text books
Course Assessment
Midterm 20%
Final Exam 60%
Class work 20%

## Slide 6: Review of prerequisite elements
Perfect gas
Thermodynamics laws
Isentropic flow
Conservation laws

## Slide 7
constant area duct
quasi one-dimensional flow
compressible flow
steady flow
isothermal flow
ideal gas
wall friction
Diameter (D)
is a constant
speed (u)
x
u varies only in x-direction
Density (ρ) is NOT a constant
Temperature (T) is a constant
Obeys the Ideal Gas equation
is the shear stress acting on the wall
where is the average Fanning friction factor
Mass flow rate is a constant

## Slide 8
Compressible Flow

## Slide 9
To be accurate, the normal differentials in the previous equation should be written as a partials.
And, if we are dealing with a perfect gas, like air,the gas state only requires knowing 3 variables.
Thus, the derivative should have a subscript indicating which 3rd variable is being held constant.
For example, if we were interested in the compressibility of a fluid at constant temperature:

## Slide 10
Alternately, it is common to consider the reversible, adiabatic (i.e isentropic) compressibility:
Both of these factors are properties of the material and can be looked up in references. Typical values are:
From the magnitude of these we get the commonly observed behavior that water (and all liquids) are much less compressible than air (and all gasses).

## Slide 11: Ideal Gas equation of state:
equation could be rearranged

## Slide 12: Perfect Gas

## Slide 13
Processes on the perfect gas

## Slide 14: Thermodynamics
Thermodynamics is the study of the way energy is stored and exchanged – a very important issue in compressible flows.
A fundamental principle is the First Law:
  The internal energy, E, of a closed system can be increased only by heat added across it’s boundaries, Q, or by work done on the system, W.
(per unit mass)

## Slide 15: Thermo. - First Law
Internal energy, E
  The energy stored in the particles themselves, I.e. random KE, rotation, vibration, chemical bonding, etc.
  e is specific internal energy, E/m, and de represents a small change in e.
Work done, dW, and Heat added, dQ
  The symbol d represents a small incremental process since both W and Q are methods of exchanging energy and not fluid properties themselves.
  the work done and heat added per unit mass of fluid are then dw and dq.

## Slide 16: Work
Only one work process is of interest in in viscid aerodynamics: the work done by squeezing a fluid element against the resistance of pressure.
Consider squeezing a sphere:
  thus
And the first law becomes
dr
p
A

## Slide 17: Enthalpy
Before proceeding, we must introduce a new fluid property, Enthalpy, given by the symbol H
Mathematically,
Or, more commonly, the specific enthalpy is defined by:
Enthalpy is the sum of the internal energy and the energy associated with having brought all the particles together into a given volume of space.

## Slide 18: Enthalpy
Small changes in specific internal energy and specific enthalpy are related by:
Therefore, the First Law can be rewritten in terms of specific enthalpy:
Note:
  Enthalpy is much more useful in aerodynamics than is internal energy.
  This is because in a flow, total enthalpy (unlike internal energy) is naturally conserved, as we will see a little later.

## Slide 19: Specific Heats
The factors relating changes in temperature to the amount of heat added are called the Specific Heats
Because heat addition is a process, we must also specify the conditions under which heat is added
At constant volume, V = constant (u = constant)
From the First Law, however:
0
thus

## Slide 20: Specific Heats
At constant pressure, p = constant
From the First Law, however:
A little note:
  In many gasses, it is possible to assume that energy is a function of temperature only, i.e. h(T) and e(T).
  This is called being thermally perfect.
  For a thermally perfect gas, the above definitions for specific heats are valid all the time, whether or not heat is actually added!
0
thus

## Slide 21: Specific Heats
Further assumptions
  We have already assumed that air is a perfect gas under most conditions, I.e. except for very high ’s and low T’s.
  Now neglect high T’s where we have to worry about vibrational excitation and dissociation of N2 and O2.
  With these restrictions, we can assume that air is calorically perfect, or that cp and cv are constants.
  The previous relations can then be integrated to get
  For convenience, we have set the zero point energies equal to zero, i.e e=h=0 when T=0.

## Slide 22: Specific Heats
Note that the specific heats are related, as shown, by the definition of enthalpy:
We will also have many equations which will have the ratio of specific heats as a factor:
This factor is strongly related to the available “modes” of energy storage – I.e. translation, rotation, vibration, electronic.

## Slide 23: Specific Heats
Thus, typical values at room temperature depend upon the molecule type:
   = 5/3 = 1.67 for monatomic gases
   = 7/5 = 1.4 for diatomic gases
    1.1 for complex, poly-atomic gases
Also, using this ratio, the specific heats can be written in terms of the specific gas constant by:
Thus, for air with R = 1716 ft2/sec2oR
  cp = 6006 ft2/sec2oR cv = 4290 ft2/sec2oR

## Slide 24: Second Law and Entropy
The determination of absolute entropy of a system can be very complex due to all the energy modes.
However, the change of entropy is known precisely from the 2nd Law of thermodynamics:
Effectively, this equation is the ratio of the energy added to a system to that which is already present.
The equation above represents a prefect world. In practice, the chaos of a system also changes whenever a system undergoes a non-equilibrium process.

## Slide 25: Second Law and Entropy
Examples of non-equilibrium process are friction, heat flux, or diffusion – or simply very fast changes.
Non-equilibrium process are irreversible – they only proceed naturally in one direction.
As a result, the full 2nd Law may be written as:
or
Unfortunately, these equations are much use for practical calculations by themselves.
To be of use, the definition of entropy must be combined with the 1st law.

## Slide 26: Entropy Calculation
The 1st law can be written in terms of either internal energy or enthalpy as:
Using the definition of entropy given before, these become:

## Slide 27: Entropy Calculation
These equations can be integrated between initial and final conditions for a calorically perfect gas:
These relations will later come in very handy in calculating the entropy change across shocks.
You may also recall using these relations in ES305 to predict the entropy at different points in a cycle.

## Slide 28: Isentropic Flow
Now consider a special situation.
First, assume no heat flux, dq = 0 or adiabatic
  A reasonable assumption; we don’t often try to heat or cool the air around an airplane!
  This does not mean the temperature remains constant - doing work can still change the energy of the fluid and thus it’s temperature.
Also, let’s assume the flow is reversible
  Thus, no friction - a reasonable assumption everywhere but near the skin surface.
  And also that there are not abrupt property changes. Abrupt changes induce dissipative losses.

## Slide 29: Thermo. - Isentropic flow
A flow which is adiabatic and reversible has constant entropy and is called isentropic.
  Practically, this means that some special relations exist between our fluid properties.
  To see this, start with the reversible, adiabatic energy equations:
  including the definitions of the specific heats:
  rearrange and divide:
0
0
or

## Slide 30: Isentropic flow
  Now, integrate over the change from one condition, 1, to another, 2:
  We can also use the perfect gas law to introduce T
or
or

## Slide 31: Isentropic flow
  To summarize, for isentropic flow, r, p and T are related by
The above equations effectively simplifies having to know 3 variables to only 2 to define a state.
This make sense since for isentropic flow, one state variable, s, is constant.
These equations can be used for many flow except for boundary layers and across shockwaves.

## Slide 32: Flow Conservation Laws
Let’s now derive the basic conservation laws for fluid flow.
We’ll use a control volume approach which implies:
  We have a volume in space of fixed size
  Fluid passes freely through the surface
For this case, a general statement of
conservation is:

## Slide 34
Conservation of mass (Steady flow)