| Benha University | Refrigeration & Air Conditioning |
| --- | --- |
| Faculty of Engineering at Shoubra | 4th Year (Power) |
| Mechanical Engineering Department | Sheet: 1 |

- A Carnot refrigeration cycle extracts 418. 68 kJ of heat per minute from a cold room which is maintained at  and it is discharged to atmosphere which is at 30. Find out the ideal power (kW) required to run the unit.

- A Carnot cycle acting as a heat pump requires 7 kW in order to supply 65 kW to a room at 26. Determine:

- Amount of heat to be removed from the source,

- Source temperature, and

- COP.

- A new refrigeration gas is said to require 1 kW for a duty of 2.5 kW when the evaporation temperature is, and the liquid is 30. Determine whether this could be true?

- The capacity of a refrigerator is 600 tons when working between  and 20. Find out the weight of ice produced within 24 hours when water is supplied at 10. Also, find out the minimum power required in kW. (Assume its cycle is a Carnot cycle).take,

- Specific heat of water

- Specific heat of ice

- Latent heat of fusion of ice at

- 2 HP per ton of refrigeration is required to maintain the temperature of  in the refrigerator. If the refrigeration cycle works on a Carnot cycle, determine:

- COP,

- Temperature of the sink,

- Heat rejected to the sink per ton of refrigeration, and

- COP if the cycle used as a heat pump.

- 100 kg of ice at  are placed in a tanker to cool some vegetables, after 24 hours later the ice melts into water at 10. What is the average rate of cooling in kJ/hr and T.R provided by the ice?

- A thermodynamic system works on the ideal Carnot cycle between a high temperature body of  and low temperature body of: (I)     (II)     (III)      (IV)        (V) 20. Determine the C.O.P of the system if working as:

- Heat Engine

- Heat Pump

- Refrigerator

Represent the results obtained on a suitable diagram, then repeat the results if the high temperature body is lower down to.

- A reversed Carnot cycle absorbs heat at  and rejects it at , calculate:

- C.O.P for the cycle when operates as a refrigerator,

- C.O.P for the cycle when operates as a heat pump,

- If the cycle is absorbing 850 kJ/min at, how many kJ of work are required per min?

- How many kJ/min will the heat pump deliver at 45 if it absorbs 850 kJ/min at ?