| Benha University | Refrigeration & Air Conditioning |
| --- | --- |
| Faculty of Engineering at Shoubra | 4th Year (Power) |
| Mechanical Engineering Department | Sheet: 2 |

- A Freon-12 refrigerating system is operating with a condensing temperature  and an evaporating temperature of. Determine:

- The refrigeration effect.

- COP.

- The system efficiency.

- A mechanical refrigerating system employing R-12 is operating with an evaporating temperature of and a condensing temperature of. If the mass flow rate of refrigerant through the system is 0.75 kg/s, determine:

- The refrigerating capacity in kW.

- The condenser capacity in kW.

- The compressor power in kW.

- The system efficiency.

- A mechanical refrigerating system employing refrigerant R-12 is operating under suction condition that the evaporator temperature is and the liquid approaching the refrigerant control is at a temperature of. If the system has a capacity of 15 kW, determine:

- The total mass flow rate of the refrigerant in kg/s.

- The total volume flow rate of the refrigerant in L/s.

- COP.

- In testing a Freon-12 refrigeration unit, the following data were recorded:

- Outlet temperature from compressor ; exit temperature from condenser  and outlet temperature from evaporator

- Rate of flow of condenser cooling water, and rise in its temperature is.

Assuming that compression is polytropic; Calculate:

- The capacity of the unit in T.R.

- COP.

- In a 15 T.R plant R-12, the condenser and evaporator temperature and respectively. Assuming wet compression with refrigerant leaves the evaporator at a dryness fraction 0.9. Assuming that compression is isentropic. Determine:

- Mass flow rate of the refrigerant.

- Compressor theoretical power.

- Condenser capacity.

- Cycle efficiency.

- Consider a 300 kJ/min refrigeration system that operates on an ideal vapor compression refrigeration cycle with refrigerant-134a as the working fluid. The refrigerant enters the compressor as saturated vapor at 140  and is compressed to 800. Show the cycle on a P-h diagram with respect to saturation lines, and determine:

- The quality of the refrigerant at the end of the throttling process.

- The coefficient of performance.

- The power input to the compressor.

- A refrigerator uses refrigerant-134a as the working fluid and operates on an ideal vapor compression refrigeration cycle between 0.12 and 0.7. The mass flow rate of the refrigerant is 0.05 kg/s. Show the cycle on a T-S diagram with respect to saturation lines. Determine:

- The rate of heat removal from the refrigerated space and the power input to the compressor.

- The rate of heat rejection to the environment.

- The coefficient of performance.