| Benha University | Refrigeration & Air Conditioning |
| --- | --- |
| Faculty of Engineering at Shoubra | 4th Year (Power) |
| Mechanical Engineering Department | Sheet: 3 |

- A vapor compression refrigeration system employing R-12 for cooling air consists of a compressor having 8 cylinders of 8.9 cm bore and 10 cm stroke running at 900 rpm, and a water-cooled condenser. The load on the plant is 5000 kJ/min. The condensing pressure is 1 and the evaporating pressure is 0.15. Refrigerant leaves the condenser as a liquid at 15, and enters the compressor at 5. The compressor delivers the refrigerant to the condenser at 79. Neglecting any pressure losses and using the following properties for R-12; calculate:

- The refrigerant mass flow rate, kg/hr.

- The volumetric efficiency of the compressor.

- The theoretical power required by the compressor.

- The COP.

- Heat reject in the condenser.

| Temperature | Pressure | Specific enthalpy | Specific volume |
| --- | --- | --- | --- |
| 5 | 0.15 | 194 | 0.123 |
| 79 | 1.00 | 232 | -------- |

Enthalpy of liquid refrigerant (sub-cooled) at.

- In a 15 T.R plant R-12, the condenser and evaporators are 35 and  respectively. Assuming wet compression with refrigerant leaves the evaporator at a dryness fraction of 0.9 and leaves the compressor at a temperature of 40. Using the following table, determine:

- Mass flow rate of refrigerant.

- Compressor theoretical power.

- Volume flow rate of refrigerant.

- Cycle efficiency.

- Cylinder diameter if the compressor has 4-cylinders of 10 cm piston stroke, a clearance volume of  and rotates atwith exponent of compression equals 1.2.

| Temperature | Pressure | Specific enthalpy | Specific entropy | Specific volume |
| --- | --- | --- | --- | --- |
| 35 | 0.847 | 233.5 | 365.4 | 1.114 | 1.542 | 0.00079 | 0.02011 |
|  | 0.261 | 195.4 | 349.3 | 0.983 | 1.557 | 0.00071 | 0.0650 |

- Heat pump working between 827 & 344. The maximum temperature in refrigerant circuit is 49. There is no under-cooling. The heat pump is used to raise the water temperature from 9 to 32 for comfortable heating. Using the following table of refrigerant properties; calculate:

- The work done by the compressor.

- The COP of heating pump.

- Mass flow rate of comfortable heating water if the refrigerant mass flow rate does not exceed 1 kg/s.

| Temperature | Pressure | Specific enthalpy | Specific entropy of vapor | Specific heat of vapor |
| --- | --- | --- | --- | --- |
| 38 | 0.827 | 128 | 484 | 1.593 | 1.003 |
|  | 0.344 | 74 | 470 | 1.697 | --------- |

- A standard vapor compression system using R-12 developing 15 T.R. the condensing temperature is 35 and the evaporating temperature is. A heat exchanger is being used between the line of suction gas to the compressor and the line of liquid leaving the condenser. The suction vapor is super heated 10. The compressor age of clearance volume is 3% with 1.2 index of compression. Assuming liquid leaves the condenser as well as vapor leaves the evaporator both are saturated and using the following table of properties of R-12 only, calculate:

- Mass flow rate of refrigerant, kg/s.

- The cycle efficiency.

- The piston stroke if the compressor runs at 1400 rpm and has 8 cylinders each 0.1 m diameter.

- Theoretical power of the compressor.

| Temperature | Pressure | Specific enthalpy | Specific entropy | Density |
| --- | --- | --- | --- | --- |
| 35 | 0.847 | 233.5 | 365.4 | 1.114 | 1.542 | 1272.98 | 49.71 |
|  | 0.261 | 195.4 | 349.3 | 0.983 | 1.557 | 1412.84 | 15.39 |
| superheat |  |  |  |  |  |  |  |
| 5 | 0.261 | ---- | 355.7 | ---- | 1.580 | ---- | 14.67 |