| Benha University Faculty of Engineering At Shoubra Industrial Engineering Dept. |  | Facilities Planning Assignment No. 1 Second term 2014/2015 |
| --- | --- | --- |

[1] A part requires three processing steps on two machines in the sequence A-B-A. The demand for this part is 10,000 units/yr. The company operates six days/week, eight hrs/day. Given the following performance data, find the number of each machine needed to meet the demand.

| operation | machine | Standard Time (min.) | Efficiency | Reliability | Defects |
| --- | --- | --- | --- | --- | --- |
| 1 2 3 | A B A | 5 3 3 | 108% 95% 90% | 98% 95% 95% | 3% 5% 5% |

[2] Given the following, what are the machine fractions for machines A, B, and C to produce parts X and Y?

|  | Machine A | Machine B | Machine C |
| --- | --- | --- | --- |
| Part X standard time Part Y standard time Part X defect estimate Part Y defect estimate Historical efficiency Reliability factor Equipment availability | 0.15 hr 0.10 hr 5% 5% 85% 95% 1600hr/yr | 0.25 hr 0.10 hr 4 % 4% 90% 90% 1600 hr/yr | hr 0.15 hr 3% 3% 95% 85% 1600 hr/yr |

Part X routing is machine A, then B, and then C; 100,000 parts are to be produced per year. Part Y routing is machine B, then A, and then C; 200,000 parts are to be produced per year. Setup times for parts X and Y are 20 minutes and 40 minutes, respectively.

[3] In a certain factory it is required to produce 2800 pieces/week., with 4% rejected pieces by using the following machine tools:

| Operation | Machine | Op. time (min.) | Dimension (Cm.) |
| --- | --- | --- | --- |
| turning milling drilling grinding assembly inspection | c. lathe H milling m/c b. drill s. grinder assembly station inspection station | 3.5 2.6 3.0 8.5 - - | 300 x 60 220 x 100(20 travel) 80 x 60 300 x 200 200 x 100 100 x 80 |

a) Calculate the number of required machines.

b) Sketch the layout of this workshop using  U flow pattern.

[4] During one eight-hour shift, 750 nondefective parts are desired from a fabrication operation. The standard time for the operation is 15 minutes. Because the machine operators are unskilled, the actual time it takes to perform the operation is 20 minutes, and, on average, one-fifth of the parts that begin fabrication are scrapped. Assuming that each of the machines used for this operation will not be available for one hour of each shift, determine the number of machines required.

[5] A factory produces 50,000 units/yr with the following conditions:

Working days/yr = 250

No. of shifts /day = 1

No. of working hours/shift = 8

Rejected products = 4%

| Op. No. | Description | Tm (min.) | Tsec (min) |
| --- | --- | --- | --- |
| 1 2 3 4 5 | Turning Shaping Drilling Milling Grinding | 4 5,5 2.8 3.4 1 | 0.67 1 0.7 0.9 9 |

- Calculate the number of machines required

- Sketch the workshop layout

[6] The stamped metal products company makes among other things a V-belt pulley. The pulley sales forecasts indicate a capacity need for 10,000 pulleys/week, the average plant efficiency is 90%. Calculate the number of needed machines, according to the following table.

| Op. No | Operation | Machine used | Standard output pieces/hr | Scrap factor % |
| --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 | Machine hub Form flange Drill and tap hub Assemble flange to hub Weld flanges together Weld flanges to hub Ream and chamfer Deburr flange Inspection | Turret lathe Punch press Drill press Arbor press Small spot welder Large spot welder Drill press Polishing lathe Inspection station | 65 4800 230 650 350 450 330 250 450 | 2 4 1 2 2 4 1 - - |

Determine the workshop area and draw with suitable scale the appropriate layout for the manufacture of the V-belt pulley, if the machines are with following dimensions:

Turret lathe/8x2/, punch press /6x3/, drill press /6x4/, arbor press /4x 1.5/,

Small spot welder /2x 0.5/, large spot welder / 2.5 x 2 /, drill press / 5x2 /,

Polish lathe /5x2/, inspection space /4x3/, raw material storage / 15x10/,

Finished goods storage / 18x10/, shear /5x1.5/ m.